## Slide 1: WF on bandwidth part configuration
OPPO, Ericsson, [Huawei], [HiSilicon], [MediaTek], [Panasonic], [Intel], [Samsung], [LGE], [Nokia], [vivo], …
3GPP TSG RAN WG1 Meeting #89 Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.7
R1-1709265

## Slide 2: Background
Working assumption (RAN1#88bis):
One or multiple bandwidth part configurations for each component carrier can be semi-statically signalled to a UE
  A bandwidth part consists of a group of contiguous PRBs
    Reserved resources can be configured within the bandwidth part
  The bandwidth of a bandwidth part equals to or is smaller than the maximal bandwidth capability supported by a UE
  The bandwidth of a bandwidth part is at least as large as the SS block bandwidth
    The bandwidth part may or may not contain the SS block
  Configuration of a bandwidth part may include the following properties
    Numerology
    Frequency location (e.g. center frequency)
    Bandwidth (e.g. number of PRBs)
  Note that it is for RRC connected mode UE
  FFS how to indicate to the UE which bandwidth part configuration (if multiple) should be assumed for resource allocation at a given time
  FFS neighbour cell RRM

## Slide 3: Discussions
  The potential use cases of bandwidth part configurations include:
    Case 1: Defining a accessible BW for a UE with bandwidth capability smaller than carrier bandwidth.
    Case 2: Further bandwidth reduction over UE bandwidth capability, e.g. for UE power saving.
    Case 3: Support resource allocation (single and/or multi-numerology resource allocation).

## Slide 4: Proposal
Specifications support configuring one or multiple bandwidth parts to a UE for DL and UL respectively for a component carrier by higher layers (FFS: dedicated RRC signaling and/or system information).
  Each bandwidth part is associated with a specific numerology (sub-carrier spacing) and consists of a number of consecutive RBs
    Indicating the frequency location with the first PRB
    FFS: other properties associated to a bandwidth part, e.g. slot duration
  For a given numerology, a UE is only assumed to receive/transmit within the active DL/UL bandwidth parts associated with the numerology.
  Specifications support configuring different bandwidth parts overlaping in frequency domain to a UE
  A default bandwidth part is for the case a UE is not configured a bandwidth part
  The number of configured bandwidth parts per UE is limited to N. FFS: N.
  FFS: Multiple bandwidth part configurations for different CORESETs, e.g. same or different for CORESETs for CSS and USS
UE expects at least one bandwidth part being active among the set of configured bandwidth parts for a given time instant in DL or UL.
  FFS: Multiple bandwidth parts can be active for a UE simultaneously
  FFS: frequency hopping of bandwidth part within one slot
  Bandwidth parts can be activated/de-activated by FFS:
    Time pattern
    DCI
      FFS: explicitly or implicitly
      FFS: Fallback machanism in case the DCI is mis-detected
    MAC CE
    ......
  Simultaneous transmission or reception on multiple bandwidth parts with different numerologies is not required from UE perspective
The set of simultaneously-active DL/UL bandwidth parts are not assumed to span a frequency range larger than the DL/UL bandwidth capability of the UE in a component carrier.
UE can adapt its RF bandwidth according to the switching of active bandwidth parts. And specifications should take account of the accommodation of UE RF retuning time.

## Slide 5: References
R1-1706900 On bandwidth part and bandwidth adaptation, Huawei, HiSilicon
R1-1707239 NR transmission on anchor bandwidth part, vivo
R1-1707420 Bandwidth part configuration and operation, Intel Corporation
R1-1707719 On bandwidth part configuration, Guangdong OPPO Mobile Telecom.
R1-1709054 On bandwidth parts, Ericsson
R1-1708017 DL Resource Allocation Aspects, Samsung