## Slide 1: WF on CRC Attachment for CBGs
Ericsson, AT&T, Fujitsu, LG, Qualcomm, MediaTek, ZTE
R1-1709271
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.4.1.1.1

## Slide 2: Background
Agreement: (RAN1#88bis)
  Number of bits for TB-level CRC is: LTB,CRC =24 bits, at least for TBs larger than a threshold (e.g. around 512 bits)
  FFS the value of LTB,CRC for TBs smaller than the threshold, and the value of the threshold (0 is not precluded)
  If a TB is segmented into 2 or more CBs after code block (CB) segmentation,
    CB-level CRC is applied, i.e., CRC bits are attached to each code block individually (as in LTE)
    Number bits for CB-level CRC is: 0 < LCB,CRC <= 24 bits
      Exact value(s) LCB,CRC are to be agreed after base graph(s) are agreed, taking into account inherent LDPC PC capability
  FFS whether for a code block group (CBG) containing 2 or more CBs but not all CBs of the TB, any additional CRC bits are attached to the CBG
    To be decide after decision on the value(s) of LCB,CRC

## Slide 3: Discussion
CBG-level CRC is not needed for producing CBG-level HARQ-feedback.
  The probability of undetected errors on CBG-level when only checking CB-level CRC is low
    Inherent syndrome checking provides probability of undetected error of CB: Pud,CB < 5x10-6
    CB-level CRC bits
CBG-level CRC is not needed for avoiding the delivery of incorrect TBs to higher layers.

## Slide 4: Proposal
For a code block group (CBG) containing 2 or more CBs but not all CBs of the TB, no additional CRC bits are attached to the CBG