## Slide 1: WF on Configuration of CSI-RS
Ericsson, AT&T, Huawei, LG, Intel, [Qualcomm],
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.2.2.1
R1-1709359

## Slide 2: Previous Agreements
Agreement:
For Connected mode, CSI-RS are supported to be configured using at least dedicated RRC signaling for DL based RRM measurement for L3 mobility.
  Note that signalling other than dedicated RRC signalling is not precluded
Working assumptions:
Beam management procedures can utilize at least the following RS type(s):
  RS defined for mobility purpose at least in connected mode
    FFS: RS can be NR-SS or CSI-RS or newly designed RS
      Others are not precluded
  CSI-RS:
    CSI-RS is UE-specifically configured
      Multiple UE may be configured with the same CSI-RS
    The signal structure for CSI-RS can be specifically optimized for the particular procedure
    Note: CSI-RS can also be used for CSI acquisition
Other RS could also be considered for beam management such as DMRS and synchronization signals
Agreement:
For UE RRC connected mode, periodic signal is supported at least for P1 procedure (Tx/Rx beam alignment) using following options in addition to UE-specifically configured CSI-RS. Down selection from following options will be conducted in the next meeting.
  Opt. 1: SS blocks
  Opt. 2: Cell-specifically configured CSI-RS
    Configuration of CSI-RS is obtained from the broadcast message (e.g., MIB, SIB)
  Opt. 3: No additional option

## Slide 3: Proposal
CSI-RS is configured only through dedicated (UE-specific) signaling
  CSI-RS configuration is not included in a broadcast message (e.g., MIB/SIB)