## Slide 1: WF on UL HARQ-ACK feedback
ZTE , Nubia
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.2.6.3
R1-1709366

## Slide 2: Background
Early PUSCH termination can be realized by UL grant for scheduling new data if eNB has new UL data to be scheduled. In this case, UL grant for scheduling new data is transmitted in advance, and no additional overhead for HARQ-ACK feedback is caused.
Early PUSCH termination can be realized by a new ACK feedback channel if eNB has no UL data to be scheduled.
For new HARQ-ACK feedback channel using PHICH-like structure, new physical resource for HARQ-ACK feedback needs to be reserved which would reduce the available resources for MPDCCH and PDSCH. Besides, the standardization effort is increased.

## Slide 3
Proposal 1
  Early PUSCH termination based on MPDCCH is supported by using the following two options:
  MPDCCH for UL grant
  MPDCCH for explicit HARQ-ACK feedback
    For explicit HARQ-ACK feedback, down select from the following two options:
      Option 1: MPDCCH for one HARQ-ACK feedback of a single PUSCH
      Option 2: MPDCCH for multiple ACK feedbacks of multiple PUSCHs
  FFS: MPDCCH search space
  FFS: For H-FDD, UL gap for MPDCCH monitoring