## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709415
Hangzhou, China, 15 - 19 May 2017
Agenda item: 6.2.5.2
WF on DMRS density reduction
Huawei, HiSilicon, China Telecom

## Slide 2: Background
Agreement in RAN1 #88bis:
Define a new DMRS table or introduce new entries in existing DMRS table
  DCI payload size is the same as legacy
Additional DMRS overhead reduction scheme for rank 3/4 transmission is FFS

## Slide 3: Proposals
New entries in DMRS table to support DMRS density reduction
  At least including the following entries in DMRS table for one and/or two enabled CWs.
    3 layers, ports 7,8,11 (OCC=4)
    4 layers, ports 7,8,11,13 (OCC=4)
    Other entries are not excluded
    FFS: introducing nscid for MU-MIMO
    FFS: new DMRS table or modification based on legacy table
Additional DMRS overhead reduction scheme for rank 3/4 transmission will not be specified in R15