## Slide 1: WF on multiple starting positions in a subframe for uplink in FeLAA
Huawei, HiSilicon, [Nokia],[…]
3GPP TSG RAN WG1 #89 R1-1709457 Hangzhou, China
15th – 19th May, 2017
Agenda item: 6.2.2.2
Document for decision

## Slide 2: Background
In the RAN1 meeting #88b, the following agreements were achieved:
  At least one additional UL starting point is introduced
    FFS: details, including whether the starting point is indicated with an UL grant or not

## Slide 3: Proposal
Only one additional UL starting point is introduced
  The additional starting point is SC-FDMA symbol #7
  UE changed to UL initial partial subframe based on LBT results
  Signaling for initial partial UL subframe
    Option 1:
      The eNB indicates if the UE could perform UL initial partial subframe by UL grant
    Option 2:
      Derive the starting positions for partial subframe ((7, 7+25us, 7+25us+TA, 7+1) from the indicator for regular subframe