## Slide 1: WF on Puncturing Methods for Polar Codes
Ericsson, MediaTek, LGE , Qualcomm
R1-1709465
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.4.2.1.2

## Slide 2: Background (1)
Puncturing is an essential process in rate matching of Polar codes whose native block lengths are powers of two.
Two types of puncturing methods are considered by all companies so far:
  Begin puncturing from the lowest code bit index, i.e. index 0.
    often referred simply as “Puncturing”
    Zero LLR is assumed to be used for punctured bits at decoder.
  Begin puncturing from the highest code bit index, i.e. index , where denote the length of mother Polar code.
    often referred simply as “Shortening”
    Infinite LLR is assumed to be used for punctured bits at decoder

## Slide 3: Background (2)
Both types are just puncturing methods
  No difference from transmitter’s point of view except for the locations of punctured code bits
  Two types are complementary of each other (R1-1704317)
“Shortening” is a misuse of terminology in this context
  Shortening is typically used in literature to refer to zero-padding when the number of available information bit locations is larger than payload, which is not the case here
Description of transmission methods should not be dictated by receiver processing (i.e. whether filling in zero or infinite LLRs for punctured bits)

## Slide 4: Proposal 1
In NR Polar code discussions, the following terminology on puncturing methods is used:
  Type I Puncturing
    The type of puncturing methods that are currently referred to as “puncturing”.
    The set of indices of punctured code bits always contain index ‘0’.
  Type II Puncturing
    The type of puncturing methods that are currently referred to as “shortening”.
    The set of indices of punctured code bits always contains index ‘N-1’.
  where N denotes the block length of the mother Polar code (which must be power-of-two), and the index set of all its coded bits are {0,1,2,⋯,N-1}.

## Slide 5: Proposal 2
In Polar code design for NR control channels, when puncturing is applied, only Type I and Type II puncturing methods are considered.

## Slide 6: Proposal 3
In Polar code design for NR control channels, nested puncturing patterns are adopted
  Nested puncturing patterns means: whenever
    For each , let denote a puncturing pattern, i.e. a set of punctured code bit indices, applied to a mother code of length to attain the target code length of .