## Slide 1: WF on Flexible PDSCH/PUSCH resource allocation for MTC
Ericsson, Orange
3GPP TSG-RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.6.6
R1-1709468

## Slide 2: Background #1
It has been observed that the misalignment between the BL/CE narrowband (NB) and the LTE resource block groups (RBG) may cause inefficient utilization of the downlink PRBs in certain traffic conditions
An example of misalignment between the BL/CE narrowband and the LTE resource block group for system bandwidth 10MHz is presented below

## Slide 3: Background #2
System BW | Total number of PRBs | RBG size | #RBGs per NB |  | # unused PRBs due to one NB |  | Effect of unused PRB |  | Description of NB set | 
 |  |  | Set #1 | Set #2 | Set #1 | Set #2 | Set #1 | Set #2 | Set #1 | Set #2
1.4 | 6 | 1 | 6 | N/A | 0 | N/A | N/A | N/A | - | 
3 | 12 | 2 | 4 | 3 | 2 | 0 | 33,3% | 0% | Low | High
5 | 25 | 2 | 3 | 4 | 0 | 2 | 0% | 10,5% | Low | High
10 | 50 | 3 | 3 | 3 | 3 | 3 | 6,8% | 6,8% | Low | High
15 | 75 | 4 | 2 | 3 | 2 | 6 | 2,9% | 8,7% | Even | Odd
20 | 100 | 4 | 2 | 2 | 2 | 2 | 2,1% | 2,1% | Low | High
The effect of the misalignment between the BL/CE narrowband and the LTE resource block groups on the possible utilization of PRBs when scheduling PDSCH on all six PRBs in one narrowband on the possible utilization of PRBs for one higher category UE is outlined in the table for all system bandwidths.

## Slide 4: Proposal
The following technique for improved PDSCH/PUSCH spectral efficiency is considered.
  Introducing support for more flexible PDSCH/PUSCH resource allocation.