## Slide 1: WF on Triggering Mechanism for CSI Reporting
NTT DOCOMO, LGE, Huawei, HiSilicon, Sharp, Mitsubishi
R1-1709485
3GPP TSG RAN WG1 Meeting #89
Agenda item: 7.1.2.3.1

## Slide 2: Background
 |  | CSI reporting |  | 
 |  | Periodic | Semi-persistent | Aperiodic
CSI-RS transmission | Periodic | CSI-RS: N/A Reporting: N/A | CSI-RS: N/A Reporting: TBD | CSI-RS: N/A Reporting: DCI
 | Semi-persistent | Not supported | CSI-RS: TBD Reporting: TBD | CSI-RS: TBD Reporting: DCI
 | Aperiodic | Not supported | Not supported | CSI-RS: DCI Reporting: DCI

## Slide 3: Background
Resource setting #1
Resource setting #2
CSI reporting setting #0
CSI reporting setting #1
Link #0
Link #1
Link #2
Link #3
Resource setting #0
CSI-RS resource set #0
CSI-RS resource set #1
CSI-RS resource set #2
CSI-RS resource

## Slide 4: Proposal
Regarding dynamic triggering,
  Semi-persistent CSI-RS is activated/deactivated by MAC CE.
  Semi-persistent CSI reporting is activated/deactivated by MAC CE.
  Selection of CSI-RS resource set for semi-persistent CSI-RS is performed by MAC CE.
  FFS: details including
    Relationship between signaling of semi-persistent CSI-RS and CSI-RS resource set selection for semi-persistent CSI-RS
    Relationship between signaling of CSI-RS transmission and CSI reporting