## Slide 1: WF on evaluation assumption for aerial vehicle
NTT DOCOMO, SoftBank, Ericsson
3GPP TSG RAN WG1 Meeting #89 R1-1709487
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 6.2.8.2

## Slide 2: Proposal
Cell layout with 37 sites, 3 sectors per site is optionally supported for evaluation.
  FFS: If it is revised to mandatory
System bandwidth: 10 MHz
BS antenna pattern for non-FD MIMO
  Antenna element pattern according to TR 36.873
  (M, N, P) = (8, 1, 2) according to TR36.873
  0.8λ spacing of vertical elements
  Companies are encouraged to report down tilt angle in their evaluations, e.g., 100 degree for UMa, 104 for UMi, 96 degree for RMa
  Note: Companies can provide additional simulation results with realistic antenna pattern
UE height (non-FD MIMO, terrestrial UE)
  Option 1: Same as FD-MIMO
  Option 2: 1.5 m
The minimum BS – Terrestrial UT distances are also used for the dropping of aerial UTs.
  FFS: Whether it is 2D distance or 3D distance
UL power control
  Companies are encouraged to report the power control parameters including Pcmax in the contributions

## Slide 3: Proposal
UT mobility (horizontal plane only)
  Terrestrial UE (outdoor): 30 km/h
  Terrestrial UE (indoor): 3 km/h
  Aerial UE: [161] km/h, horizontal only
  Note: Velocity of aerial UE can be revised according to RAN2 agreement
Number of aerial UE
  Case 1: 0 UE per sector for reference
  Case 2: 1 UE per 10 sectors
  Case 3: 1 UE per sector
  Case 4: 3 UEs per sector
  Case 5: 5 UEs per sector
  Note: Companies are encouraged to provide evaluation results at least for case 1 and case 5.
Number of total UE per sector is 15

## Slide 4: Proposal
Traffic model
  For terrestrial UE, data type traffic is assumed in downlink and uplink
    Packet size of 0.5 MB
    Packet arrival rate is selected to achieve resource utilization values of 20% and 50% including resource utilization of aerial UEs
  For aerial UE, command and control traffic is assumed in downlink and data type traffic is assumed in uplink
    Command and control traffic in DL
      Periodic traffic with fixed packet size is assumed:
        FFS: inter-packet arrival time interval of D
        FFS: packet size X
      Note: X is determined based on the requirement on DL data rate and latency for command and control traffic. and D can be revised according to RAN2 agreement.
    Data type traffic in UL
      Same traffic model including packet size and packet arrival rate as for terrestrial UE

## Slide 5: Proposal
Scheduler assumption
  No QoS, i.e. command and control traffic and data traffic are handled with equal priority by the scheduler