## Slide 1: WF on bandwidth part configuration
OPPO, Ericsson, Huawei, HiSilicon, MediaTek, Intel, DOCOMO, LGE, ETRI, CATR, NEC, ZTE, CATT, Samsung, [vivo], [NOKIA], [AT&T], [Panasonic]
3GPP TSG RAN WG1 Meeting #89 Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.7
R1-1709519

## Slide 2: Background
Working assumption (RAN1#88bis):
One or multiple bandwidth part configurations for each component carrier can be semi-statically signalled to a UE
  A bandwidth part consists of a group of contiguous PRBs
    Reserved resources can be configured within the bandwidth part
  The bandwidth of a bandwidth part equals to or is smaller than the maximal bandwidth capability supported by a UE
  The bandwidth of a bandwidth part is at least as large as the SS block bandwidth
    The bandwidth part may or may not contain the SS block
  Configuration of a bandwidth part may include the following properties
    Numerology
    Frequency location (e.g. center frequency)
    Bandwidth (e.g. number of PRBs)
  Note that it is for RRC connected mode UE
  FFS how to indicate to the UE which bandwidth part configuration (if multiple) should be assumed for resource allocation at a given time
  FFS neighbour cell RRM

## Slide 3: Proposal
Confirm the WA of RAN1#88bis.
Each bandwidth part is associated with a specific numerology (sub-carrier spacing, CP type)
  FFS: slot duration indication if RAN1 decides to not to downselect between 7 symbol and 14 symbols for NR slot duration
UE expects at least one DL bandwidth part and one UL bandwidth part being active among the set of configured bandwidth parts for a given time instant.
  A UE is only assumed to receive/transmit within active DL/UL bandwidth part(s) using the associated numerology
    At least PDSCH and/or PDCCH for DL and PUCCH and/or PUSCH for UL
      FFS: down selection of combinations
  FFS if multiple bandwidth parts with same or different numerologies can be active for a UE simultaneously
    It does not imply that it is required for UE to support different numerologies at the same instance.
    FFS: TB to bandwidth part mapping
  FFS: activate/de-activate machanism
The active DL/UL bandwidth part is not assumed to span a frequency range larger than the DL/UL bandwidth capability of the UE in a component carrier.
Specify necessary mechanism to enable UE RF retuning for bandwidth part switching