## Slide 1: WF on Open Aspects of Short TTI Evaluation Methodology for V2V Communication
Intel, LG Electronics
3GPP TSG RAN WG1 Meeting #89 R1-1709526
Hangzhou, P.R. China, 15th – 19th May, 2017
Agenda item – 6.2.3.3.1

## Slide 2: Background
At the RAN1#88-bis meeting, system-level evaluation assumptions for sTTI analysis were discussed
RAN1#88-bis conclusion:
  “continue discussion at RAN1#89 and make a decision on whether to model ADC quantization errors. For next meeting, companies are encouraged to explain how and if quantization noise is modelled”

## Slide 3: SQNR vs ADC Scaling
SQNR depends on RX signal backoff with respect to ADC scale
RX power deviations within subframe can cause significant SINR variations and performance loss for R14 UEs

## Slide 4: Proposal 1
ADC quantization errors (AGC impact) are taken into account in system level evaluations of short TTI performance
Agree on the single number of ADC bits to be used for baseline system level evaluations - e.g. 8 bits (< 12 bits)
SQNR curve is used to take into account ADC quantization and clipping noise

## Slide 5: Proposal 2
Two approaches are considered to model ADC quantization errors in system level analysis
  Approach 1 (Quantization Noise)
  Approach 2 (Quantization & Clipping Noise)
Note
  Approach 1 is applicable when shared AGC symbol is assumed
  Approach 2 is applicable when shared AGC symbol is not assumed

## Slide 6: Proposal 3
Perform system level evaluation of short TTI transmissions using Approach 1, if shared AGC symbol is assumed
Approach 1 (Quantization Noise)
  In this approach, all TX UEs transmit at the 1st symbol of subframe and RX UEs use it to settle AGC
  In this approach, with proper signal scaling (BO settings), only quantization noise can be considered (i.e. no clipping)
  SQNR curve can be used to determine quantization noise

## Slide 7: Proposal 4
Perform evaluation using Approach 2 if shared AGC symbol is not assumed
Approach 2 (Quantization and Clipping Noise)
  ADC backoff (BO) is set to [-18dB]
    For R14 UEs, BO is evaluated with respect to RX power at the 1st symbol of subframe
    For R15 UEs, BO is set with respect to the 1st symbol of short TTI
  Spectrally flat quantization and clipping noise is assumed
  UE calculattes RX power level (P1) used for AGC settling
  UE calculates RX power level (P2) in demodulation symbol

## Slide 8: Proposal 4 (Continued)
Approach 2 (Quantization and Clipping Noise)
  P2 and P1 are used to determine the SNR per symbol (using SQNR curve)
  If (P2 < P1), then only quantization noise is added
  If P1 < P2 < (P1 +Threshold), then both quantization and clipping noise are added
  If (P2 > P1+Threshold), reception is declared as failed
  Threshold = [10 dB]