## Slide 1: WF on Codebook Based UL-MIMO Transmission
Huawei, HiSilicon, Samsung
3GPP TSG RAN WG1 Meeting #89 R1-1709548
Hangzhou, China, 15 -19 May 2017
Agenda item – 7.1.2.1.3

## Slide 2: Background
Agreements in RAN1 meeting #88bis:
Codebook based transmission for UL is supported at least by following signaling in UL grant:
  SRI+TPMI+TRI, where
    The TPMI is used to indicate preferred precoder over the SRS ports in the selected SRS resource by the SRI.
    No SRI when a single SRS resource is configured
      The TPMI is used to indicate preferred precoder over the SRS ports in the configured single SRS resource.
  Support indication on selection of multiple SRS resources
    FFS details
For codebook based transmission for CP-OFDM based UL, when a UE is configured with UL frequency selective precoding and if subband TPMI signaling is supported, support one of the following alternatives:
  Alt 1:Subband TPMIs are signaled via DCI to the UE only for allocated PRBs for a given PUSCH transmission
  Alt 2:Subband TPMIs are signaled via DCI to the UE for all PRBs in UL, regardless of the actual RA for a given PUSCH transmission
  Other alternatives are not precluded
  Note: Subband TPMI may correspond to W2 if dual-stage codebook is supported
FFS whether or not wideband TPMI is always signaled along with subband TPMI

## Slide 3: Proposal
For UL frequency selective precoding, NR supports subband TPMI indication to the UE via DCI for the allocated PRBs only
  Subband TPMIs are signaled in the second stage DCI if two-stage-DCI is supported
Support at least two-stage codebook in NR for codebook based UL-MIMO
On top of indication of multiple SRS resources selection, support signaling to indicate TPMI across the selected multiple SRS resources in the UL grant for PUSCH precoder determination