## Slide 1: Analysis of SSS Proposals
Intel
3GPP TSG RAN WG1 Meeting RAN1 #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.1.1.1
Document for: Discussion and Decision
R1-1709550

## Slide 2: Basic Properties
Company | Number of PSS Seq. | Number of SSS Seq. | Number of PCID | Sequence Type | Additional Notes
Intel [1] | 3 | 381 | 1143 | single famliy gold-like | 
Intel – Alternate | 3 | 381 | 1143 | single famliy gold-like | 
MediaTek [2] | 3 | 336 | 1008 | single family m-seq x z4 | complex scrambling
LGE [3] | 3 | 336 | 1008 | single family m-seq x m-seq x m-seq | 5ms scrambling
Motorola [4] | 3 | 334 | 1002 | single famliy gold-like* | 20ms scrambling
Samsung [5] | 1 | 1016 | 1016 | multi-family m-seq | 
Nokia [6] | 3 | 381 | 1143 | single famliy gold-like | 
Huawei [7] | 3 | 336 | 1008 | single famliy gold-like | 
ZTE – Option 1 [8] | 3 | 381 | 1143 | single family gold-like | no PSS scrambling
ZTE – Option 2 [8] | 3 | 381 | 1143 | multi-family gold-like | no PSS scrambling
Docomo [9] | 3 | 334 | 1002 | multi-family gold-like | 
Qualcomm [10] | 3 | 381 | 1143 | multi-family gold-like | mid-amble permutation
Interdigital [11] | 3 | 381 | 1143 | multi-family gold-like | 
Ericsson – Option 1 [12] | 3 | 381 | 1143 | multi-family gold-like | 
Ericsson – Option 2 [12] | 3 | 381 | 1143 | single family truncated long x short m-seq | 
CATT – Option 1 [13] | 3 | 336 | 1008 | multi-family gold-like | 
CATT – Option 2 [13] | 3 | 336 | 1008 | multi-family gold-like | 
CATT – Option 3 [13] | 3 | 336 | 1008 | single family m-seq x m-seq x m-seq | 
*: Motorola [4] has a scrambling on top of the single family gold-like sequence (multiplication of 3 sequence)

## Slide 3: PAPR & CM Analysis
Sequence Type | Company | Median PAPR | Max PAPR | Median CM+ | Max CM+
single famliy gold-like | Intel [1] | 7.626 | 9.948 | 3.882 | 5.445
single famliy gold-like | Intel – Alternate | 7.642 | 10.32 | 3.908 | 5.465
single famliy gold-like* | Motorola [4] | 7.474 | 11.25 | 3.794 | 7.124
single famliy gold-like | Nokia [6] | 7.543 | 9.772 | 3.883 | 6.129
single famliy gold-like | Huawei [7] | 7.561 | 11.28 | 3.895 | 6.24
single famliy gold-like | ZTE – Option 1 [8] | 7.579 | 10.84 | 3.867 | 6.349
single family truncated long x short m-seq | Ericsson – Option 2 [12] | 7.454 | 10.41 | 3.82 | 6.182
single family m-seq x z4 | MediaTek [2] | 7.356 | 9.52 | 3.664 | 4.65
single family m-seq x m-seq x m-seq | LGE [3] | 7.377 | 12.85 | 3.775 | 9.249
single family m-seq x m-seq x m-seq | CATT – Option 3 [13] | 7.387 | 10.53 | 3.754 | 6.589
multi-family m-seq | Samsung [5] | 5.749 | 7.716 | 1.964 | 2.981
multi-family gold-like | ZTE – Option 2 [8] | 5.332 | 6.684 | 1.233 | 1.944
multi-family gold-like | Docomo [9] | 7.269 | 10.94 | 3.712 | 7.372
multi-family gold-like | Qualcomm [10] | 7.494 | 11.11 | 3.845 | 6.939
multi-family gold-like | Interdigital [11] | 7.516 | 12.1 | 3.834 | 9.229
multi-family gold-like | Ericsson – Option 1 [12] | 7.569 | 11.16 | 3.851 | 7.009
multi-family gold-like | CATT – Option 1 [13] | 7.157 | 11.03 | 3.608 | 7.561
multi-family gold-like | CATT – Option 2 [13] | 7.409 | 11.22 | 3.811 | 7.372
*: Motorola [4] has a scrambling on top of the single family gold-like sequence (multiplication of 3 sequence)
+: CM was computed using CM reference of 1.5237 and CM normalization of 1.56
All PAPR and CM were computed with 64 oversampled sync interpolated time domain waveform

## Slide 4: PSS-SSS Cross Correlation
Sequence Type | Company | Maximum Normalized Cross Correlation (Time Domain) |  |  |  |  | 
 |  | CFO 0% |  |  | ±140% Subcarrier CFO |  | 
 |  | PSS #1 | PSS #2 | PSS #3 | PSS #1 | PSS #2 | PSS #3
single famliy gold-like | Intel [1] | 0.2671 | 0.2687 | 0.282 | 0.2844 | 0.3095 | 0.297
single famliy gold-like | Intel – Alternate | 0.2854 | 0.2858 | 0.2829 | 0.2985 | 0.2997 | 0.3062
single famliy gold-like* | Motorola [4] | 0.288 | 0.2904 | 0.2768 | 0.4325 | 0.3425 | 0.3576
single famliy gold-like | Nokia [6] | 0.2865 | 0.2913 | 0.3128 | 0.3183 | 0.3118 | 0.3169
single famliy gold-like | Huawei [7] | 0.2812 | 0.2693 | 0.2756 | 0.3375 | 0.3133 | 0.318
single famliy gold-like | ZTE – Option 1 [8] | 0.2738 | 0.2763 | 0.2606 | 0.2997 | 0.2832 | 0.2914
single family truncated long x short m-seq | Ericsson – Option 2 [12] | 0.2913 | 0.3071 | 0.3228 | 0.3677 | 0.3453 | 0.3524
single family m-seq x z4 | MediaTek [2] | 0.2491 | 0.2578 | 0.253 | 0.2923 | 0.2937 | 0.2825
single family m-seq x m-seq x m-seq | LGE [3] | 0.3055 | 0.2913 | 0.2756 | 0.385 | 0.3399 | 0.316
single family m-seq x m-seq x m-seq | CATT – Option 3 [13] | 0.3161 | 0.2913 | 0.3093 | 0.3216 | 0.3209 | 0.3136
multi-family m-seq | Samsung [5] | 0.5354 | 0.5197 | 0.5512 | 0.601 | 0.5721 | 0.6152
multi-family gold-like | ZTE – Option 2 [8] | 0.3228 | 0.3228 | 0.3228 | 0.3335 | 0.3253 | 0.325
multi-family gold-like | Docomo [9] | 0.3228 | 0.3228 | 0.3228 | 0.3253 | 0.3335 | 0.3432
multi-family gold-like | Qualcomm [10] | 0.3228 | 0.2964 | 0.3228 | 0.342 | 0.3199 | 0.3754
multi-family gold-like | Interdigital [11] | 0.3228 | 0.3228 | 0.3228 | 0.3841 | 0.3494 | 0.3374
multi-family gold-like | Ericsson – Option 1 [12] | 0.3071 | 0.2837 | 0.2929 | 0.315 | 0.315 | 0.3166
multi-family gold-like | CATT – Option 1 [13] | 0.3228 | 0.3228 | 0.3228 | 0.3603 | 0.3636 | 0.3432
multi-family gold-like | CATT – Option 2 [13] | 0.3228 | 0.3228 | 0.3228 | 0.3603 | 0.3634 | 0.3432
*: Motorola [4] has a scrambling on top of the single family gold-like sequence (multiplication of 3 sequence)

## Slide 5: SSS-SSS Cross Correlation
Sequence Type | Company Name | CFO 0% |  | CFO 0.15% | CFO 0.30%
 |  | Median X-Corr | Max X-Corr | Max X-Corr | Max X-Corr
single famliy gold-like | Intel [1] | 0.0079 | 0.1339 | 0.3 | 0.4779
single famliy gold-like | Intel – Alternate | 0.0079 | 0.1339 | 0.2439 | 0.336
single famliy gold-like | Motorola [4] | 0.0079 | 0.1339 | 0.2301 | 0.3053
single famliy gold-like | Nokia [6] | 0.0079 | 0.1339 | 0.3028 | 0.482
single famliy gold-like | Huawei [7] | 0.0079 | 0.1339 | 0.3023 | 0.4816
single famliy gold-like | ZTE – Option 1 [8] | 0.0079 | 1 | 1 | 1+
single family truncated long x short m-seq | Ericsson – Option 2 [12] | 0.0551 | 0.3228 | 0.4472 | 0.5534
single family m-seq x z4 | MediaTek [2] | 0.0837 | 0.0948 |  | 0.2854
single family m-seq x m-seq x m-seq | LGE [3] | 0.0079 | 0.2598 | 0.3307 | 0.3742
single family m-seq x m-seq x m-seq | CATT – Option 3 [13] | 0.0551 | 0.3228 | 0.3869 | 0.5231
multi-family m-seq | Samsung [5] | 0.0551 | 0.3228 | 0.3374 | 0.3808
multi-family gold-like | ZTE – Option 2 [8] | 0.0079 | 1 | 1 | 1+
multi-family gold-like | Docomo [9] | 0.0551 | 0.3543 | 0.4464 | 0.5831
multi-family gold-like | Qualcomm [10] | 0.0551 | 0.4488 | 0.4558 | 0.4558
multi-family gold-like | Interdigital [11] | 0.0551 | 0.3228 | 0.4441 | 0.5789
multi-family gold-like | Ericsson – Option 1 [12] | 0.0551 | 0.3228 | 0.4555 | 0.5958
multi-family gold-like | CATT – Option 1 [13] | 0.0551 | 0.3228 | 0.4464 | 0.5831
multi-family gold-like | CATT – Option 2 [13] | 0.0551 | 0.3701 | 0.4576 | 0.5981
+: cross correlation of ‘1’ is stemming from lack of PSS based scrambling for SSS

## Slide 6: Intel – Alternative SSS Proposal
 | First Sequence | Second Sequence
Polynomials | g0(x) = x7+x4+1 | g1(x) = x7+x6+x5+x4+x3+x2+1
Cyclic Shifts | 10,15,18,28,30,52,55,57,111 | 0,1,2,…,126
Single Family Gold-Like Sequence

## Slide 7: Residual CFO in SSS Detection
Residual CFO is limited to
less than 30% of subcarrier spacing in 99% of the cases at -6dB
Less than 15% of subcarrier spacing in 85% of the cases at -6dB

## Slide 8: References
[1] R1-1707336, “Remaining Details on SS Sequence Design,” 3GPP RAN1 #89, Intel Corp.
[2] R1-1707829, “NR SSS Design and Evaluation,” 3GPP RAN1 #89, MediaTek
[3] R1-1707587, “NR SS sequence design,” 3GPP RAN1 #89, LG Electronics
[4] R1-1708302, “NR-SS sequence design and evaluation ,” 3GPP RAN1 #89, Motorola Mobility, Lenovo
[5] R1-1707926, “Remaining Details of SS Sequence Design,” 3GPP RAN1 #89, Samsung
[6] R1-1708231, “Remaining details on SS sequence design,” 3GPP RAN1 #89, Nokia, Alcatel-Lucent Shanghai Bell
[7] R1-1708160, “Remaining details for synchronization signals ,” 3GPP RAN1 #89, Huawei, HiSilicon
[8] R1-1707042, “NR-SS sequence design and evaluation,” 3GPP RAN1 #89, ZTE
[9] R1-1708436, “Discussion and evaluation on NR-SS sequence design ,” 3GPP RAN1 #89, NTT DOCOMO, INC.
[10] R1-1708568, “Synchronization signal sequence design,” 3GPP RAN1 #89, Qualcomm Incorporated
[11] R1-1707457, “NR-PSS and NR-SSS Sequence Design ” 3GPP RAN1 #89, CATT