## Slide 1: Offline outcome regarding radio link monitoring
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #89 R1-1709555
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.5.3
Document for decision

## Slide 2: Background
R1-1706870
Q1: Can the in-sync/out-of-sync indications for RLF be provided per cell?
Q2: Is RAN1 planning to provide in-sync/out-of-sync indications that are periodic (similar to LTE)?

## Slide 3: Offline outcome
IS and OOS indications are based on SINR-like metric (e.g., hypothetical PDCCH BLER) as in LTE
  SINR-like metric as in LTE represents whether or not UE can receive PDCCH
  FFS: PDCCH in U-SS and/or PDCCH in C-SS
RS used to derive SINR-like metric is down selected from following options
  Opt.1: CSI-RS
  Opt.2: DMRS for NR-PDCCH in C-SS
  Opt.3: DMRS for NR-PBCH
  Opt.4: NR-SSS
  Opt.5: RS for time/frequency tracking (if separate RS from above is defined for time/frequency tracking)
  FFS: how many options are used
RAN1 assumes that single IS or OOS is indicated per reporting instance regardless number of beams available in cell. RAN1 has not concluded whether IS/OOS indications for RLF are per cell or not.
RAN1 plans to provide periodic IS/OOS indications.
  FFS: possibility of additional aperiodic IS indication e.g., based on beam failure recovery mechanism.

## Slide 4: Proposed reply
Q1: Can the in-sync/out-of-sync indications for RLF be provided per cell?
A1: RAN1 assumes that single IS or OOS is indicated per reporting instance regardless number of beams available in cell. RAN1 has not concluded whether IS/OOS indications for RLF are per cell or not.
Q2: Is RAN1 planning to provide in-sync/out-of-sync indications that are periodic (similar to LTE)?
A2: RAN1 plans to provide periodic IS/OOS indications.