## Slide 1: WF on UL Sharing for NSA NR UE
Apple Inc, Huawei, HiSilicon, Deusche Telecom, Samsung, Orange, OPPO, vivo, INL, [Vodafone], […]
3GPP TSG RAN WG1 #89 Meeting R1-1709586
Hangzhou, P.R.China, 15-19th May 2017

## Slide 2: Background (1/2)
NR initial deployment will likely be non-stand alone (NSA)
  NSA uses dual connectivity.
  Control plane uses LTE, user plane uses NR
In general, dual connectivity requires two active radio links in both uplink and downlink.
From UE implementation perspective, simultaneous uplink transmissions can create various intermodulation product, leading to serious downlink sensitivity degradation.

## Slide 3: Background (2/2)
To give a few examples: It was agreed in RAN4#82bis that LTE and NR carrier aggregation band combinations with LTE_4DL/1UL CC (B1,3,7,20) + NR_1DL/1UL CC (3.4-3.8GHz) is to be supported [7].
  The IM5 produced at the NR transmitter from the 2nd harmonic of Band 3 uplink (1710-1785 MHz) and NR uplink (3.3-3.8 GHz) could well fall into the Band 7 downlink frequencies (2620-2690 MHz) under the above 4DL/1UL CC (B1,3,7,20) + NR_1DL/1UL CC (3.4-3.8GHz) simultaneous dual uplink operation.
  Similarly, a simultaneous 4th order harmonic of uplink transmission at Band 20 and NR uplink transmission can also create IM5 intermodulation product interfering Band 7 downlink reception and thus desense the Band 7 receiver.
  This issue would not only happen in LTE-NR DC case, for NR only case if there are two UL frequencies as the above, similar problem would occur.

## Slide 4: Proposal
UE configured with multiple UL carriers on different frequencies should not be assumed to necessarily support simultaneous transmission on both carriers.
  For the case of LTE/NR dual-connectivity, the detailed solution(s) to avoid simultaneous transmission from a single UE on both carriers is expected to be resolved no later than NSA frozen time.
  For the standalone case, NR should allow one UL carrier transmission at one time.
  Note: this does not preclude SRS to be sent on NR uplink

## Slide 5: Appendix (1/2)
In NR WID:
NR-LTE co-existence mechanisms [RAN1, RAN2, RAN4];
- Support co-existence of LTE UL and NR UL within the bandwidth of an LTE component carrier and co-existence of LTE DL and NR DL within the bandwidth of an LTE component carrier, and identify and specify at least one NR band/LTE-NR band combination for this operation.
  - Minimize impact to NR physical layer design to enable this co-existence.
  - No impact to the ability of legacy LTE devices to operate on the LTE carrier co-existing with NR
  - No implication that UE has to support simultaneous connection of NR and LTE in the bandwidth of an LTE component carrier

## Slide 6: Appendix (2/2)
LTE-NR co-existence should support the following UL sharing scenarios:
  Collocated LTE and NR base stations with network operating UL on frequency F1 where LTE UL and NR UL share UL subframes of LTE
    Detailed sharing on the UL is FFS
      Note: this is not intended to have impact on legacy LTE UEs
    LTE DL on a paired frequency F3
    NR DL transmission on frequency F2 (different than LTE DL frequency)
    NR UE operates in either of the following cases based on a common NR design:
      Standalone NR: UE accesses standalone NR carrier on F2. The UE may not be connected to an LTE carrier (some UE may not even support LTE).
        FFS whether NR UL frequency F1 is signaled in NR broadcast system information or derived from MIB/PBCH, or implicitly from NR DL frequency F2
      Dual connectivity of LTE and NR: UE accesses LTE PCell (with LTE UL on F1), then is configured by dual connectivity to also operate NR on F1 (UL) and F2 (DL).
        NR DL and UL frequencies (and/or NR band number) are signaled by RRC
  Non-collocated LTE and NR base stations is FFS