## Slide 1: WF on RS design requirement for fine time and frequency tracking
MediaTek, Huawei, Hisilicon, Ericsson, Samsung [Qualcomm, Intel]
3GPP TSG RAN WG1 #89
Hangzhou, China, 15th – 19th May 2017
Agenda item: 7.1.2.4.6
R1-1709640

## Slide 2: Background
The summary of issues and views on fine time and frequency of channel is provided in R1-1709290

## Slide 3: Proposals
RS for fine/time frequency tracking is denoted as TRS
  Whether the term “TRS” appear in specifications is FFS
The TRS framework includes burst structure and TRS structure inside a burst
The parameters for burst structure are at least
  X: the length of TRS burst in terms of number of slots
  Y: the TRS burst periodicity in terms of number of slots
Slot
Slot
Slot
…
Slot
Slot
Slot
Slot
Slot
…
Slot
Slot
Each TRS bust spans X Slots
One TRS burst for every Y slots
One TRS burst for every Y slots
Each TRS bust spans X Slots
(figure from R1-1708602)

## Slide 4: Proposals
The parameters for TRS structure inside a burst are least
  Sf: TRS subcarrier spacing
  St: TRS symbol spacing within a slot
  N: Number of OFDM symbols per TRS within a slot
  B: TRS bandwidth in terms of number of RBs
The different slots in a TRS burst may have different TRS parameters (N,B, Sf , St ) (FFS)
TRS has an equal RE spacing in frequency domain
  FFS: Whether multiple values are supported
TRS may have a repetition or staggered structure in time domain within a slot
  FFS: Whether symbol spacing is equal or non-equal within slot
TRS supports a single port
  FFS: Other numbers of TRS ports, resources, etc.
FFS on TRS configuration details

## Slide 5: Proposals
Determine the required set or sets of RS parameters on previous pages for appropriate tracking performance in various scenarios
  Bring simulation results in next meeting
  Note Multiple sets and configurability may be needed to meet various scenarios
After RS parameters are defined, determine which RS(s) for time delay tracking, frequency offset tracking, delay spread estimation and Doppler spread estimation
  RS(s) can be the existing ones, revision of the existing ones, or new ones
  The extension to multi-beam, multi-TRP are considered

## Slide 6: Candidate parameters for evaluation
Candidates for TRS subcarrier spacing (Sf)
  1,4,6
  Other values not precluded
  Note: in one TRS burst, different Sf can be used for different symbols
Candidates for TRS symbol spacing (St)
  2, 3,4,7
  Combination of two values (1,3)
  Non-equal symbol spacing within the slot
  Other values not precluded
0
0
1
2
3
4
5
6
7
8
9
10
11
12
13
Example: marked by green

## Slide 7: Candidate parameters for evaluation
Candidate values of the number of OFDM symbols (N) per TRS are
  1,2,4
  Other values not precluded

## Slide 8: Candidate parameters for evaluation
Candidates for the value B (TRS bandwidth)
  Alt 1: 50RBs. The granularity is 0.11us for SCS=15KHz (1/(SCSx 12 xRB number) )
  Alt 2: 24RBs. The granularity is 0.23us for SCS=15KHz
  Alt 3: Up to the transmission bandwidth configuration
  Alt.4: 12RBs
  Note: need to consider the uplink transmission error requirement defined in 36.133
  Other bandwidths are not precluded
Study the minimum required value of B

## Slide 9: Candidate parameters for evaluation
Candidate TRS burst length (X)
  1,2
  Other values not precluded
Candidate TRS periodicity values (Y)
  5,10,20
  Y Implicitly determined by SS block periodicity
  Other values not precluded

## Slide 10: Reference Examples
LTE CRS: X=1, Y=1, Sf= 6, St= (3,4), N=4, B= channel bandwidth
LTE CSI-RS: X=1, Y= configured period, Sf=12, St = 14xY, N=1, B=channel bandwidth
NR SSS: X=1, Y=20, Sf=1, St=14xY, N=1, B=10.5