## Slide 1: NR UL MIMO Signaling Mechanism
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm, CATT, ZTE
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15 -19 May 2017
Agenda item – 7.1.2.1.3
R1-1709673

## Slide 2: Background
UL MIMO related signaling is supported via DCI, but available payload size is unclear
  In RAN1#87, it was agreed to support at least wideband TPMI
  In RAN1#88bis, it was agreed to support SRI+TPMI+TRI in a UL grant
TPMI+TRI+SRI should fit in single stage DCI report
  Dual stage DCI will be done later in Rel-15, and in worst case may not be supported in Rel-15, i.e. from RAN1#88:
    Two-stage DCI is expected to be discussed further after more details of the design for the single-stage DCI are known.
It is expected that DCI payloads will have similar size to LTE to allow similar coverage to LTE.
LTE uses up to 12 bits for UL MIMO
  Up to 6 bits 4 Tx precoding + TRI;
  5 bits are used for MCS and RV of a second transport block
  1 bit for a new data indicator of a second transport block

## Slide 3: Proposal
TPMI, SRI, and TRI are carried in single stage DCI
Study further the maximum size of TPMI, SRI, and TRI and their combinations
  Note: ~10 bits can be used as an initial estimate