## Slide 1: WF on NR-RACH preamble format for coverage enhancement
ZTE, CMCC
3GPP TSG RAN WG1 Ad Hoc Meeting
HangZhou, China 15th – 19th March 2017
Agenda: 7.1.1.4.1
R1-1709708

## Slide 2: Observations regarding necessity for UMa coverage enhancement
The supportable cell radius is shrinked due to higher carrier frequency in NR (e.g. around 4GHz for UMa) if PRACH MCL is not enhanced
Increasing MCL with 6dB compared with LTE format 0 can help to keep similar ISD.
LTE preamble format 2 have 3dB higher MCL than LTE preamble format 0.

## Slide 3: Proposal on premble formats for L = 839 and coverage enhancement
Format | L | SCS(kHz) | BW (MHz) | N_OS | N_RP | T_SEQ (Ts) | T_CP (Ts) | T_GP (Ts) | Use case
4 (3.5ms) | 839 | 1.25 | 1.08 | 4 | 1 | 4*24576 | 4688 | 4528 | Coverage enhancement
Note:
L is the sequence length
Ts = 1/(30720) ms
Proposal: Introduce a PRACH preamble format that
provides 3dB MCL gain compared to LTE PRACH preamble format 2.