## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709771
Hangzhou, China, 15-19 May 2017
Agenda item: 7.1.1.5.2
WF on CSI-RS properties for L3 mobility
Huawei, HiSilicon, …

## Slide 2: Background(1)
In RAN1#88bis, some agreements were achieved for CSI-RS for L3 mobility:
For CONNECTED mode RRM measurement for L3 mobility based on CSI-RS, NR supports following targets for CSI-RS design and configuration:
Design:
  Reuse CSI-RS design for beam management as baseline
  Identify additional requirements on the CSI-RS to support L3 mobility
Configuration:
  Support measurement of a large number of beams
  Minimize configuration overhead, reporting overhead, and UE complexity
  FFS: Detailed signaling or format
For Connected mode, CSI-RS are supported to be configured using at least dedicated RRC signaling for DL based RRM measurement for L3 mobility.
  Note that signalling other than dedicated RRC signalling is not precluded
The time synchronization reference for a CSI-RS for L3 mobility is the frame/slot/symbol timing of a cell.
  Note: The frame/slot/symbol timing of the cell can be obtained from an SS block
  FFS: Note: timing synchronization between CSI-RS and SS block of the cell is assured. Timing synchronization refers to frame/slot/symbol timing.
NR cell ID for time reference of CSI-RS(s) is informed to the UE

## Slide 3: Background(2)
Clarify previous RAN1 agreements on the RSRP definition for DL RRM measurements for L3 mobility as follows
  Define SS block RSRP and CSI-RS RSRP as
    SS block RSRP : measured RSRP from SSS
      FFS additional use of PBCH-DMRS for measurement
    CSI-RS RSRP : measured RSRP from CSI-RS in connected mode
Conclusions:
For Mobility
Following remaining issues need to be finalized in the next meeting
  Properties of CSI-RS for RRM measurement for L3 mobility, e.g.,
    Timing of CSI-RS for RRM measurement for L3 mobility
    Bandwidth of CSI-RS for RRM measurement for L3 mobility
    Numerology of CSI-RS for RRM measurement for L3 mobility
    The number of REs in the freq. domain of CSI-RS for RRM measurement for L3 mobility
    Resource mapping and parameters of CSI-RS for RRM measurement for L3 mobility
    Configuration of CSI-RS parameters for RRM measurement for L3 mobility

## Slide 4: Background(3)
In RAN1#89, some agreements were achieved for CSI-RS properties for L3 mobility:
Following CSI-RS properties for RRM measurement for L3 mobility are supported in NR
  Periodic CSI-RS transmission with configurable periodicity
    Note that CSI-RS transmission can be turned on and off
    FFS: candidate periodicity values
  Configurable transmission/measurement bandwidth
    FFS: whether/how transmission and/or measurement bandwidth is indicated to UE
  Configurable CSI-RS time/frequency resource
    Note that this property is the same with that for beam management based on CSI-RS
    Note that the numerology for CSI-RS should consider neighbor cell measurement aspects

## Slide 5: Proposal
At least the following properties of CSI-RS for L3 mobility are signalled to the UE using dedicated signaling:
  NR Cell ID
  timing configuration, including time offset and periodicity
  number of antenna ports
  configurable time/frequency resource
  Configurable scrambling ID
  configurable transmission/measurement bandwidth
  FFS: configurable numerology
  FFS: Spatial QCL assumption e.g. QCL between SS block and CSI-RS
FFS: Number of CSI-RS resources configured in this configuration