## Slide 1: WF on Alternative DL Tx Beam Indication in Msg. 3 for RACH Procedure in Multi-Beam Scenario
AT&T, Qualcomm
3GPP TSG-RAN WG1 #89 R1-1709776
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.1.4.2

## Slide 2: Background
During RAN1#88bis the following conclusion was made :
Conclusions:
NR studies following beam management options for RACH procedure:
  Beam refinement procedure during Msg2
    Note: P-2/P-3 procedure can be considered for beam refinement
  Reporting of DL TX beam indices in Msg3
    Note: reported beams could be SS block indices and/or CSI-RS beam indices of P-2 procedure performed during Msg2
  RACH procedure using an association between CSI-RS for L3 mobility and subset of RACH resources and/or subset of RACH preamble indices
  Beam refinement procedure before Msg2 by utilizing CSI-RS for L3 mobility
  Beam refinement procedure during or after Msg4 by configuration in RACH message
  Reporting UE capability on beam correspondence by RACH procedure
  Other options are not precluded
  Above procedure can be turned on/off by system information

## Slide 3: Background
Enhancing beam management during RACH procedure by reporting more than one beam index and/or quality will improve the reliability of beam management for IDLE and CONNECTED mode UEs
Alternative DL Tx beam reporting in RACH Msg. 3:

## Slide 4: Proposal
NR should support explicit alternative DL Tx beam indication in msg. 3.
Whether or not the alternative DL Tx beam in msg. 3 should be reported can be indicated to the UE.