## Slide 1
WF on DL PRB Bundling Size Value Set
Xinwei, HW, HiSilicon, CATT, MTK, Intel, ZTE
3GPP TSG RAN WG1 RAN1 #89
Hangzhou, China, 15th – 19th May 2017
Agenda item: 7.1.2.1.6
R1-1709791

## Slide 2: Background
Agreements:
For PRB bundling of data channel
  Support common design for PRB bundling for different scenarios, e.g. channel reciprocal or non-reciprocal, different Tx/Rx beamforming, etc:
    Specify common PRB bundling size set for all scenarios
      FFS: Different PRB bundling size sets for different BWs
    Specify common indication procedure for all scenarios
  The following PRB bundling sizes are studied:
    Specified value(s) X:
      FFS X
      FFS whether more than one value is needed.
      Strive for value aligned with resource allocation granularity
    Contiguous allocated PRBs when at least Y contiguous PRBs are allocated. FFS: values of Y;
    Scheduled BW dependent, FFS the relationship
    Values equal or larger than scheduled BW
    FFS different transmission schemes may be related to different subsets of PRB bundling configurations
    Others are not precluded;
  Support UE specific PRB bundling size indication:
    FFS: RRC configured with a subset, DCI dynamically indicated
      DCI overhead should be considered;
        MAC CE can be considered if the number of subset elements are large, details FFS
      FFS: the presence of DCI field related to PRB bundling is configured by RRC;
    FFS: Implicit signaling to inform PRB bundling size can be considered
  FFS UE feedback assisted PRB bundling size

## Slide 3: Proposals
For DL data transmission
  PRB bundling size include
    Category 1: value(s) aligned with RBG
      FFS X=1 and X=2;
      FFS X=4;
      FFS RBG/k, where k is integer, FFS whether k is always equal to 1
      FFS m by RBG, where m is integer, FFS whether m is always equal to 1
    Category 2: other values based on bandwidth part, scheduled bandwidth and/or UE capability etc.
      E.g., Consecutive scheduled bandwidth
        FFS restrictions
      E.g., Values equal or larger than scheduled BW
        FFS restrictions
    FFS other categories;
    FFS the relationship between above values with e.g. DMRS patterns
  FFS UE feedback assisted PRB bundling size with respect to UE complexity, feedback overhead increase and performance gains.
  FFS joint or separate indication of PRB bundling size on data and DMRS