## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709777
Hangzhou, China, 15th – 17th May 2017
Agenda item: 7.1.1.4.1
WF on PRACH preamble format for NR new use cases
MediaTek, CHTTL, Intel

## Slide 2: Background (1/3)
Agreements at RAN1 #89 on beam failure recovery:
Support the following channel(s) for beam failure recovery request transmission:
  Non-contention based channel based on PRACH, which uses a resource orthogonal to resources of other PRACH transmissions, at least for the FDM case
    FFS other ways of achieving orthogonality, e.g., CDM/TDM with other PRACH resources
    FFS whether or not have different sequence and/or format than those of PRACH for other purposes
    Note: this does not prevent PRACH design optimization attempt for beam failure recovery request transmission from other agenda item
    FFS: Retransmission behavior on this PRACH resource is similar to regular RACH procedure
  Support using PUCCH for beam failure recovery request transmission
    FFS whether PUCCH is with beam sweeping or not
    Note: this may or may not impact PUCCH design
  FFS Contention-based PRACH resources as supplement to contention-free beam failure recovery resources
    From traditional RACH resource pool
    4-step RACH procedure is used
    Note: contention-based PRACH resources is used e.g., if a new candidate beam does not have resources for contention-free PRACH-like transmission
FFS whether a UE is semi-statically configured to use one of them or both, if both, whether or not support dynamic selection of one of the channel(s) by a UE if the UE is configured with both

## Slide 3: Background (2/3)
Agreements at RAN2 97bis meeting for on demand request for SI transmission
1: For idle and inactive mode, there will be network control whether MSG1 or MSG3 can be used to transmit SI request.
2: If the PRACH preamble and/or PRACH resource specific to each SIB or set of SIBs which the UE needs to acquire is included in minimum SI then SI request is indicated using MSG 1.
3: If the PRACH preamble and/or PRACH resource specific to each SIB or set of SIBs which the UE needs to acquire is not included in minimum SI then SI request is included in MSG3.
FFS Error handing in case SI is not received
FFS whether the request delivered in MSG 3 can be used for unicast delivery or for delivery of SI by dedicated signalling after a transition into connected, or other options

## Slide 4: Background (3/3)
Preamble formats discussed in RAN1 #89
  Use cases that have been considered do not include beam recovery requests and on demand SI requests.
Format | L | SCS(kHz) | BW (MHz) | N_OS | N_RP | T_SEQ (Ts) | T_CP (Ts) | T_GP (Ts) | Use case
0 | 839 | 1.25 | 1.08 | 1 | 1 | 24576 | 3168 | 2975 | LTE refarming
1 | 839 | 1.25 | 1.08 | 2 | 1 | 2*24576 | 21024 | 21904 | Large cell, upto 100km
3 (1ms) | 839 | 5 | 4.32 | 4 | 1 | 4*6144 | 3168 | 2976 | High speed case
4 (3.5ms) | 839 | 1.25 | 1.08 | 4 | 1 | 4*24576 | 4690 | 4526 | Coverage enhancement

## Slide 5: Problem Statement
NR supports new uplink requests such as beam recovery requests and on demand SI requests that did not exist in LTE.
PRACH channel has been agreed to be used for on demand SI request and is very likely to be agreed to be used for beam recovery request at this meeting.
  Beam recovery request resources can be FDM/TDM/CDM to PRACH resources.
However, these two new use cases have not been discussed in RACH design in the Initial Access agenda item.

## Slide 6: Proposal
Consider NR new use cases, including beam recovery requests and on demand SI requests, in PRACH preamble format design.
Study the following aspects:
  requirements to satisfy above new use cases
  impact on capacity
  whether additional preamble format(s) is needed