## Slide 1
3GPP TSG RAN WG1 Meeting RAN1#88bis R1-1709263
Hangzhou, China, 15th – 19th May, 2017
Agenda item: 7.1.1.1.2
WF on NR SS block composition
Huawei, HiSilicon, …

## Slide 2: Background
It was concluded in RAN1#88bis that
  Mapping of NR-PSS, NR-SSS and NR-PBCH to SS block of SS burst set configurations needs to be finalized in this meeting.
Working assumption
  NR-PSS, NR-SSS and NR-PBCH are presented in every SS block
    FFS: deactivated cell case (if defined)
The following agreements were achieved in RAN1 #88bis,
  Number of symbols per SS block
    1 symbol NR-PSS
    1 symbol NR-SSS
    2, 3 or 4 symbols NR-PBCH (to be decided once the payload and NR-PBCH design has been agreed)
  FFS: Multiplexing of TSS/TSCH in SS block if TSS/TSCH is agreed to be introduced
  In a single SS block, the symbols are consecutive
  The number of antenna ports of NR-SSS is 1
    FFS: indication of radio frame boundary by NR-SSS
  PBCH BW: 288 subcarriers, 2 OFDM symbols (additional symbols if MIB size larger than assumed)

## Slide 3: Proposal
For SS block composition, the following should be supported
  Confirm the working assumption that NR-PSS, NR-SSS and NR-PBCH are present in every SS block
  NR-SSS is mapped at the adjacent position of at least one of NR-PBCH symbols
  NR-PSS is mapped before NR-SSS.
  The mapping order of SS blocks is PSS-SSS-PBCH-PBCH.