## Slide 1: Way Forward on CSI-RS for Beam Management
Intel, InterDigital, Samsung, MediaTek, Nokia, Alcatel Lucent Shanghai Bell, CATT, KT, NEC, Xinwei, Ericsson, Qualcomm, ZTE, China Telecom, vivo, AT&T, OPPO, LG, Huawei, Hisilicon
3GPP TSG RAN WG1 Meeting #89 R1-1709303
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.2.4.1

## Slide 2: Background
In RAN1 #88bis, the following working assumption on CSI-RS for beam management has been agreed:
  For CSI-RS for Beam Management, NR supports sub-time units equal to and smaller than an OFDM symbol in a reference numerology
    FFS details including configurability, e.g., taking into account UE implementation complexity/capability and impact on CSI-RS design
    FFS the case of time unit larger than an OFDM symbol in a reference numerology
    E.g.,
      Opt-1: IFDMA
      Opt-2: Larger subcarrier spacing
      Opt-3: DFT-based

## Slide 3: Background
RAN4 confirmed agreements in RAN1 in LS R1-1706877
  SCS supported for bands below 1 GHz
    15kHz, 30kHz
    The decision of supporting 60kHz is pending RAN1 check
  SCS supported for bands between 1GHz and 6GHz
    15kHz, 30kHz, 60kHz
  SCS supported for bands above 24GHz and below 52.6GHz
    60 kHz, 120kHz
    240kHz is not applicable for data
  240kHz for data can be further considered if a clear benefit is shown
  SCS support is band dependent
  RAN4 assumes others SCS at least for data may be added in a forward compatible manner in later releases

## Slide 4: Background (cont’d)
In RAN1 #88, the following agreements on CSI-RS for beam management have been achieved:
  For beam management overhead and latency reduction, NR considers following options for a CSI-RS supporting beam sweeping within an OFDM symbol
    Opt-1: IFDMA [e.g., R1-1700350, R1-1703179]
    Opt-2: Larger subcarrier spacing [e.g., R1-1700350, R1-1701813]
    Opt-3: DFT-based [e.g., R1-1702329, R1-1703179]
    Other options are not precluded
    If supported, down-selection among the options during WI phase
    Note: the symbol duration is based on a reference numerology

## Slide 5: Background (cont’d)
In RAN1 #87 meeting, the following agreements have been achieved:
CSI-RS supports the DL Tx beam sweeping and UE Rx beam sweeping
NOTE: CSI-RS can be used in P1, P2, P3
NR CSI-RS supports the following mapping structure
  NP CSI-RS port(s) can be mapped per (sub)time unit
    Across (sub)time units, same CSI-RS antenna ports can be mapped
    Values of NP is FFS
    Here, “time unit” refers to n>=1 OFDM symbols in a configured/reference numerology, where the value of n is FFS
      FFS whether OFDM symbols comprising a time unit is consecutive or not
    FFS Port multiplexing method, e.g., FDM, TDM, CDM, any combinations
  Each time unit can be partitioned into sub-time units
    FFS Partitioning method, e.g., TDM, IFDMA, OFDM symbol-level partition with same/shorter OFDM symbol length(i.e. larger subcarrier spacing)
    as/than the reference OFDM symbol length (subcarrier spacing), and other methods are not precluded
  This mapping structure can be used for supporting multiple panels/Tx chains
  Options to map CSI-RS for Tx and Rx beam sweeping for further study
    Option 1:
      Tx beam(s) are same across sub-time units within each time unit
      Tx beam(s) are different across time units
    Option 2:
      Tx beam(s) are different across sub-time units within each time unit
      Tx beam(s) are same across time units
    Option 3: combination of Alt1 and Alt2:
      Within one time unit, Tx beam(s) are same across sub-time units.
      Within another time unit, Tx beam(s) are different across sub-time units.
      FFS combination of the different time units in terms of e.g., number and periodicity
    Note that only Tx sweeping or Rx sweeping is also a possibility
    Other options are not precluded.
    FFS: how to capture “same beam” and “different beam” in spec
FFS: Whether the above mapping structure is configured with one or multiple CSI-RS resource configurations

## Slide 6: Proposal
Confirm the WA of CSI-RS for Beam Management in RAN1 #88bis.
Down-select from the below options when sub-time unit smaller than an OFDM symbol in a reference numerology:
  Opt-1: IFDMA
  Opt-2: Larger subcarrier spacing
  Opt-3: DFT-based
For beam management, the reference numerology is the numerology configured for the bandwidth part.