## Slide 1: WF on additional DMRS structure
Samsung, Qualcomm Incorporated, Ericsson, CATT, Nokia, Alcatel-Lucent Shanghai Bell, vivo, Mitsubishi Electric Co., NTT DOCOMO, INC., ETRI, KT Corp., MediaTek Inc.
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.2.4.2
R1-1709305

## Slide 2: Background
The followings were agreed in RAN1#88bis
Companies are encouraged to perform further evaluations on additional DM-RS symbols, using same or lower density compared with front loaded DM-RS, and also identifying use cases associated with the operation.
  Aim to decide in the next meeting whether to support same density only, or lower density only, or both
FFS at least CP-OFDM, frequency domain density of front loaded DMRS is configurable.

## Slide 3: Background
R1-1707973 shows the following results for additional DMRS structure with different options
Opt-1
Opt-2 (Pattern1)
Opt-2 (Pattern2)
Throughput performance of additional time domain DMRS structures
(UE speed=300km/h, CDL-A with DS value=300ns)

## Slide 4: Background
R1-1708598 shows the following results for additional DMRS structure with different options
Configuring an additional DMRS with reduced density compared to the front-load DMRS leads to clear performance losses across a variety of scenarios.
TDL-A 100 nsec with 120 kmh
TDL-B 100 nsec with 120 kmh
TDL-C 300 nsec with 120 kmh

## Slide 5: Background
R1-1708094 shows the following results for additional DMRS structure with different options
CDL-D (DS = 10ns, K-factor = 13.3dB)
UE Speed = 500 km/h
16QAM 3/4
Spectral efficiency is improved when front-loaded DMRS and additional DMRS have the same frequency-domain density

## Slide 6: Background
R1-1709027 shows the following results for additional DMRS structure with different options in the high speed train scenario at 30GHz
Equal density 1
Equal density 2
Unequal density 1
Unequal density 2
Time and Frequency domain averaging, K=13.3dB
Time and frequency domain interpolation, K=7dB
Observation: In the high speed train scenario, equal or unequal density of DMRS configuration does not have significant impact on the spectral efficiency performance
Proposal: Consider the equal DMRS density design

## Slide 7: Proposals
Support additional DMRS symbols with same density in frequency domain compared to front loaded DMRS.
At least for DL CP-OFDM, frequency domain density of front loaded DMRS is configurable.