## Slide 1: Way forward on narrowband measurement accuracy enhancement
Huawei, HiSilicon, [….]
R1-1709372
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.2

## Slide 2: Background
Agreements from RAN1#88bis:
At least NSSS is used additionally to NRS for in-band, guard-band, standalone.
  FFS details of related signaling
Additional candidates can be NPSS, NPBCH, NPRS, PRS (in-band), CRS (in-band), physical signal that can be efficiently decoded or detected prior to decoding NPDCCH/NPDSCH (if standardized) and the performance improvements should be evaluated until RAN1#89
  Among the additional candidates, companies are recommended to prioritise CRS (in-band)
  FFS if the existing signal(s)/channel(s) used additionally to NRS can be different in the serving cell to a neighbour cell
FFS for RRC_connected mode where at least the NPDCCH could be helpful for narrowband measurement accuracy improvement
FFS details of how UE is informed of differing EPRE between signals

## Slide 3: Proposals
  For RRC_IDLE UE, NSSS is the only additional signal for RRM measurement enhancement in Rel-15.
    RAN1 observes that NSSS combined with NRS may not be always as good as NSSS only, depending on relative SNR condition
    How to use, i.e. if and/or when to combine NRS with NSSS depend on RAN4 study, and specification implementation may be joint between RAN1 and RAN4.
For RRC_CONNECTED UE, it is feasible from RAN1 point of view to use NPBCH and/or NSSS on an anchor carrier in the serving cell, and RAN4 are requested to consider if they are suitable transmissions for RRM measurement
Send an LS containing the above to RAN4