## Slide 1: WF on CSI timing
LG Electronics, ZTE, Intel, InterDigital, NTT DOCOMO, Samsung, [Qualcomm], Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, [Huawei], …
R1-1709396
3GPP TSG RAN1 #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda Item: 7.1.2.3.1

## Slide 2: Agreements in RAN1 Jan. Adhoc
Agreements:
For aperiodic CSI-RS timing offset X, support X=0 at least, if aperiodic CSI-RS triggering is done by DCI
  FFS: supporting other values of X
  Note: ‘aperiodic CSI-RS timing offset X’ refers to the time gap between aperiodic CSI-RS triggering and aperiodic CSI-RS transmission w.r.t. number of slots.
For CSI reporting timing offset Y that is fixed or configurable by the network but with certain restriction on lower limit of Y to provide sufficient CSI computation time.
  Candidate values of Y are fixed or pre-determined by certain rule(s).
    Rule is FFS (e.g. number of CSI measurement/RS/reporting settings, CSI feedback type, number of ports, nearest CSI-RS transmission timing, UE capability, etc.)
  Note: ‘aperiodic CSI reporting timing offset Y’ refers to the time gap between aperiodic CSI reporting triggering and aperiodic CSI reporting w.r.t. number of slots.
  FFS Y is fixed or configurable
  FFS configuration is done by DCI and/or MAC CE and/or higher layer signaling

## Slide 3: Proposals (1/2)
For aperiodic CSI-RS triggering offset X, X is fixed to zero.
For aperiodic CSI reporting triggering offset Y, NR supports multiple values of Y.
  Values of Y include 0.
  Values of Y also include at least one of 3 and 4.
  FFS on additional values of Y

## Slide 4: Proposals (2/2)
Y can be configured in reporting setting by RRC.
  Allowed/disallowed conditions are defined at least for Y=0.
    Y=0 is supported in DL-UL mixed slot structure only.
    If PMI is included as a CSI reporting parameter, Y=0 is allowed under the following conditions:
      the number of CSI-RS antenna ports measured is 2
      the codebook is type I
      CSI-RS is transmitted no later than the Z-th OFDM symbol in a slot; Value of Z is FFS.
    Other conditions are FFS
    FFS: whether to define allowed/disallowed conditions for other values of Y
  FFS on mechanisms to relax CSI reporting timing offset according to number of simultaneous CSI calculations
  FFS how many of the N CSI reporting settings a UE is able to compute at a given time
CSI-RS(s) received after the slot in which aperiodic CSI reporting triggering DCI is received is not taken into account for the CSI calculation.