## Slide 1: WF on HARQ process handling when switching between 1ms TTI and sTTI
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell
R1-1709444
3GPP TSG RAN1 #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.2.1.2.1.3

## Slide 2: Background
During the study item the following agreement was made
  For PUSCH transmission in sTTI (sPUSCH for short TTI), a UE can be dynamically (with a subframe to subframe granularity) scheduled with PUSCH and/or sPUSCH.
In RAN1#87 the following agreement was made
  A UE can be dynamically (with a subframe to subframe granularity) scheduled with legacy TTI unicast PDSCH and/or short TTI unicast PDSCH
In order not to induce losses when dynamically switching between 1ms TTI and sTTI, HARQ process sharing between 1ms TTI and sTTI is needed

## Slide 3: Proposal
On a carrier configured with sTTI operation and shortened processing time (N+3) for 1ms TTI for a UE:
  For a HARQ process scheduled from USS, the retransmission can have a different TTI length than an earlier transmission of the same HARQ process
    FFS: soft-buffer management in the UE
    FFS: TX buffer management in the UE
  The number of HARQ processes for
    sTTI is 16
    1ms TTI with N+3 scheduled from USS is 16
    1ms TTI scheduled from CSS is 8