## Slide 1: WF on handling beam failure recovery for unexpected cases
3GPP TSG RAN WG1 Meeting #89 R1-1709498
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.2.2.2
vivo, Qualcomm

## Slide 2: Background
The following agreements on beam failure recovery have been achieved in RAN1# 88bis meeting:
UE Beam failure recovery mechanism includes the following aspects
  Beam failure detection
  New candidate beam identification
  Beam failure recovery request transmission
  UE monitors gNB response for beam failure recovery request
Beam failure detection
  UE monitors beam failure detection RS to assess if a beam failure trigger condition has been met
  Beam failure detection RS at least includes periodic CSI-RS for beam management
    SS-block within the serving cell can be considered, if SS-block is also used in beam management as well
  FFS: Trigger condition for declaring beam failure
New candidate beam identification
  UE monitors beam identification RS to find a new candidate beam
  Beam identification RS includes
    Periodic CSI-RS for beam management, if it is configured by NW
    Periodic CSI-RS and SS-blocks within the serving cell, if SS-block is also used in beam management as well
Beam failure recovery request transmission
  Information carried by beam failure recovery request includes at least one followings
    Explicit/implicit information about identifying UE and new gNB TX beam information
    Explicit/implicit information about identifying UE and whether or not new candidate beam exists
    FFS:
      Information indicating UE beam failure
      Additional information, e.g., new beam quality
  Down-selection between the following options for beam failure recovery request transmission
    PRACH
    PUCCH
    PRACH-like (e.g.,different parameter for preamble sequence from PRACH)
  Beam failure recovery request resource/signal may be additionally used for scheduling request
UE monitors a control channel search space to receive gNB response for beam failure recovery request
  FFS: the control channel search space can be same or different from the current control channel search space associated with serving BPLs
  FFS: UE further reaction if gNB does not receive beam failure recovery request transmission

## Slide 3: Proposals
  For UE monitors a control channel search space to receive gNB response for beam failure recovery request(s), detection of a gNB’s response for beam failure recovery request during a predetermined or configured time window should be supported.
    If not detected, UE notifies higher layer entities.