## Slide 1: WF on PTRS position for CP-OFDM
3GPP TSG RAN WG1 Meeting #89 R1-1709502
Hangzhou, China, 15th – 19th May, 2017
Agenda Item: 7.1.2.4.3
ZTE, vivo, Nokia, Alcatel-Lucent Shanghai Bell, Xinwei, ASTRI, Ericsson, Huawei, HiSilicon, Samsung, LG Electronics, NTT DOCOMO

## Slide 2: Background
Agreements in RAN1#88bis meeting
For CP-OFDM, the same PTRS to RE mapping and PTRS densities in time and frequency are available for DL and UL
Distributed PTRS (non-consecutive subcarriers) in the frequency domain is used as default configuration
    FFS: Support optional frequency-localized pattern with UE-specific explicit signaling. (e.g. higher MCS case)
For single-user case, support orthogonal multiplexing among PTRS ports, if multiple PTRS antenna ports are supported.
    FFS: how to multiplex multiple PTRS ports, e.g. FDM, TDM, CDM
    FFS: Whether to support multiple PTRS ports or not (FFS: Max number of PTRS APs).
Support orthogonal multiplexing between PTRS and data transmitted or received by a single UE.
For MU-MIMO, non-orthogonal multiplexing of e.g. PTRS/PTRS and PTRS/data is possible but also orthogonal multiplexing to be considered
FFS: Support multiplexing through multiple scrambling sequences for PTRS port(s)
Support association between PTRS port and DMRS port group
Notes: i

## Slide 3: Proposal
  The RBs containing PTRS can be derived from the scheduled RBs and the associated frequency density
  For a given RB, if present, one PTRS port should be mapped on one or more subcarrier(s) carrying one or more DMRS ports of the associated DMRS port group
    FFS: to support different subcarriers by complementary option
  Support non-overlapping between PTRS and CSI-RS
    FFS whether PTRS or CSI-RS should be punctured or shifted on overlapping part if PTRS and CSI-RS are collided
  Support non-overlapping between PTRS and SRS
    FFS whether PTRS or SRS should be punctured or shifted on overlapping part if PTRS and SRS are collided
  Support non-overlapping between PTRS and SS block
    FFS whether PTRS or SS block should be punctured or shifted on overlapping part if PTRS and SS block are collided
Notes: i