## Slide 1: WF on NR-RACH preamble format for coverage enhancement
ZTE
3GPP TSG RAN WG1 Ad Hoc Meeting
HangZhou, China 15th – 19th March 2017
Agenda: 7.1.1.4.1
R1-1709574

## Slide 2: Requirements for coverage enhancement
UE speed: 120km/h
Carrier frequency: Up to 6GHz
TRP and UE clock accuracy: 0.05 ppm at TRP, 0.1 ppm at UE
Cell radius: Up to 5km
MCL target: 148dB @500m from gNB (cover indoor Ues, large penetration loss)

## Slide 3: Proposal on premble formats for L = 839 and coverage enhancement
Format | L | SCS(kHz) | BW (MHz) | N_OS | N_RP | T_SEQ (Ts) | T_CP (Ts) | T_GP (Ts) | Use case
4-A (3.5ms) | 839 | 1.25 | 1.08 | 4 | 1 | 4*24576 | 4690 | 4526 | Coverage enhancement
4-B (3.5ms) | 839 | 2.5 | 2.16 | 8 | 1 | 8*12288 | 4690 | 4526 | Coverage enhancement
4-C (2ms) | 839 | 2.5 | 2.16 | 4 | 1 | 4*12288 | 6240 | 6048 | Coverage enhancement
Note:
L is the sequence lenght
Ts = 1/(30720) ms
Select one of 4-A, 4-B and 4-C