## Slide 1: WF on CSI timing
LG Electronics, AT&T, KT Corp., Xinwei, WILUS Inc., InterDigital, Samsung, ZTE
R1-1709609
3GPP TSG RAN1 #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda Item: 7.1.2.3.1

## Slide 2: Agreements in RAN1 Jan. Adhoc
Agreements:
For aperiodic CSI-RS timing offset X, support X=0 at least, if aperiodic CSI-RS triggering is done by DCI
  FFS: supporting other values of X
  Note: ‘aperiodic CSI-RS timing offset X’ refers to the time gap between aperiodic CSI-RS triggering and aperiodic CSI-RS transmission w.r.t. number of slots.
For CSI reporting timing offset Y that is fixed or configurable by the network but with certain restriction on lower limit of Y to provide sufficient CSI computation time.
  Candidate values of Y are fixed or pre-determined by certain rule(s).
    Rule is FFS (e.g. number of CSI measurement/RS/reporting settings, CSI feedback type, number of ports, nearest CSI-RS transmission timing, UE capability, etc.)
  Note: ‘aperiodic CSI reporting timing offset Y’ refers to the time gap between aperiodic CSI reporting triggering and aperiodic CSI reporting w.r.t. number of slots.
  FFS Y is fixed or configurable
  FFS configuration is done by DCI and/or MAC CE and/or higher layer signaling

## Slide 3: Agreements in RAN1 Jan. Adhoc
Agreements:
Timing between DL assignment and corresponding DL data transmission is indicated by a field in the DCI from a set of values
  The set of values is configured by higher layer
Timing between UL assignment and corresponding UL data transmission is indicated by a field in the DCI from a set of values
  The set of values is configured by higher layer
Timing between DL data reception and corresponding acknowledgement is indicated by a field in the DCI from a set of values
  The set of values is configured by higher layer
Timing(s) is (are) defined at least for the case where the timing(s) is (are) unknown to the UE
  FFS the value for the timing

## Slide 4: Proposals
For aperiodic CSI reporting on PUSCH, Y is indicated by DCI.
  DCI to be used for indicating the timing for PUSCH allocation is also used to indicate Y.
    Timing between UL assignment and corresponding PUSCH is within the candidate set of values of Y.
  This applies without regard to the decision on supporting either or both cases of UCI multiplexing with data on PUSCH and UCI only on PUSCH.
  NOTE: Agreement in RAN1 Jan. Ad-hoc:
    Timing between UL assignment and corresponding UL data transmission is indicated by a field in the DCI from a set of values
      The set of values is configured by higher layer
The candidate set of values of Y is selected according to restricted conditions inferred from configuration of CSI related settings.
  The condition include at least;
    CSI parameter
    Number of CSI-RS antenna ports if PMI is included
    CSI-RS location
    Frequency granularity of CSI
    FFS: number of simultaneous CSI calculations
  FFS on mechanisms to relax CSI report timing according to number of simultaneous CSI calculations
  FFS different or same conditions for the cases of UCI multiplexed with data and UCI only
FFS: aperiodic CSI reporting on PUCCH