## Slide 1: WF on SRS sequence generation
Mitsubishi Electric, Huawei, HiSilicon, Nokia, AT&T, Intel, ZTE, LG Electronics, Panasonic, Ericsson
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.2.4.4
R1-1709699

## Slide 2: Background
Agreement related to SRS sequence generation in RAN1#88bis
Support configurable SRS sequence ID by UE specific configuration if SRS sequence ID is supported
  Configuration examples:
    higher layer
high layer + L1 signalling, If hierarchical indication of SRS sequence ID is supported, (example: base sequence ID and/or phase rotation ID)
Agreement related to SRS sequence in RAN1#89
ZC based sequences shall be used for NR SRS sequence design

## Slide 3
Objective of this WF: Agree on the following for ZC sequence generation
  How root number for ZC is determined
  Whether to support Sequence ID or not
  Configuration of sequence ID
Background

## Slide 4: Proposals
Support SRS sequence ID to generate SRS sequences where SRS sequence ID is UE specifically configured using
  RRC
  FFS: UE specific ID (example: C-RNTI) which can be overwritten by RRC signaling
  FFS: for combination of RRC and DCI
Root(s) of Zadoff-Chu based sequence(s) of an SRS sequence is at least a function of SRS sequence ID
  FFS on details of the function,
  Examples:
    The function is parameterized only by SRS sequence ID
    The function is parameterized by SRS sequence ID, length of SRS sequence, SRS sequence scheduled time
    The function is a random number generator, intended for sequence hopping, with a SRS sequence ID as a random seed
    The function is parameterized by SRS sequence ID, scheduled time and frequency location of the SRS sequence
FFS: SRS sequence generation details, e.g., block wise sequence generation and concatenation (one/multiple roots), long sequence based designs (one root), etc.