## Slide 1: WF on PRACH capacity enhancement
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #89 R1-1709700
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.4.1
Document for decision

## Slide 2: Background
Agreements:
For Zadoff-Chu sequence type, the RAN1 specifications will support two NR-PRACH sequence lengths (L)
  L = 839: SCS = {1.25, 2.5, 5} KHz
  Select one of
    L = 63/71: SCS = {15, 30, 60, 120, 240} KHz
    L = 127/139: SCS = {7.5, 15, 30, 60, 120} KHz
  FFS: Supported subcarrier spacings for each sequence length
FFS for other sequence types
Agreements:
NR RACH capacity shall be at least as high as in LTE
  Such capacity is achieved by time/code/frequency multiplexing for a given total amount of time/frequency resources
Zadoff-Chu sequence is adopted in NR
  FFS other sequence type and / or other methods in addition to Zadoff-Chu sequence for the scenario, e.g., high speed and large cells
    FFS definition of large cell and high speed
  FFS other sequence type and / or other methods for capacity enhancements, e.g.:
    At least in multi-beam and low speed scenario, regarding multiple/repeated PRACH preamble formats, option 2 with OCC across preambles
      FFS: Option 2 with OCC across multiple/repeated preambles in high speed scenarios
    PRACH preamble design composed with multiple different ZC sequences
    Sinusoidal modulation on top of option 1

## Slide 3: Background
When short sequence length, i.e. 63/71 or 127/139, is applied, capacity is decreased due to smaller number of available root sequence and CS.
However multiple RACH resources can be configured to compensate the lack of capacity even when short sequence length is applied.

## Slide 4: Discussion
RAN1 should discuss on the necessity of following solutions for further capacity enhancement, in addition to flexible capacity control based on multiple RACH resources.
  Solution 1: option1 with Sinusoidal modulation
  Solution 2: option2 with OCC
  Solution 3: option4 with different sequence
  Solution 4: Zadoff-Chu sequence with m-sequence cover sequences

## Slide 5: Conclusion
Continue study on necessity of RACH capacity enhancement and possible solutions (if capacity enhancement is necessary) until next meeting with considering at least following aspects
  Capacity limit due to short sequence length (e.g., which can be applied to beam sweeping)
  Capacity due to higher subcarrier spacing
  Supported cell radius as function of PRACH preamble reuse distance
  Capacity impact due to cell radius impact on Ncs
  Possibility to exploit spatial separation
  Arrival rate of UEs within a beam/cell
  UE distribution within cell