## Slide 1: WF on RACH sequence for high speed large radius cells
Nokia, Alcatel-Lucent Shanghai Bell, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, USA 15th - 19th May 2017
Agenda Item: 7.1.1.4.1
R1-1709711

## Slide 2: Background
RAN1#89
Offline working assumption:
NR supports PRACH preamble formats 3-A for the sequence length of 839.
  FFS on restricted set
  FFS other sequence(s) for large cell radius

## Slide 3: Some Calculations
UE speed 500 Km/hr, Fc=6 GHz, clock accuracy: 0.1 ppm (gNB), 0.05 ppm (UE)
Max frequency offset ~ 6.5 KHz
Assuming LTE-like restricted sets and SCS = 5 KHz:
  Type A  Ncs_max = 237  radius < 8.5 Km
  Type B  Ncs_max = 137  radius < 4.9 Km

## Slide 4: Proposal
NR should support RACH preamble sequence that is more resilient to frequency offsets and supports larger cell radius than the Zadoff-Chu sequence.
NR supports Cyclic delay-Doppler shifted M-Sequences for high speed, large cell-radius cells.