## Slide 1: WF on NR-PBCH contents and payload size
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #89 R1-1709754
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.2.1
Document for decision

## Slide 2: Background
Agreements:
RAN1 targets design of NR PBCH to be no larger than [100 bits] and no less than 40 bits including CRC.
  This simply provide guidance for potential minimum and maximum value.
Agreements:
NR-PBCH provides configuration information for the NR-PDCCH scheduling the NR-PDSCH carrying the remaining minimum system information
  FFS if a part of configuration information can be derived by specification
Agreements:
Down-select one of SCS options for the remaining minimum system information transmission
  Option 1: PBCH signals the SCS of the remaining minimum system information
  Option 2: The same SCS applied in PBCH transmission is used for the transmission of the remaining minimum system information
  FFS whether the SCS refers to the control and/or data channel for remaining minimum system information
  Note: RAN2 has decided to go with option 2

## Slide 3: Background
Agreements:
The following methods are considered for the indication of which of the nominal SS blocks in SS burst sets that are actually transmitted:
  PBCH
  Remaining minimum system information
  Other SI
  dedicated signaling
  Other methods are not precluded
Consider flexibility and signaling overhead.
Note that nominal SS block is the possible SS block time location
Note that the number and positions of the nominally transmitted SS blocks in an SS burst set is predefined.
Agreements:
Time index indication: PBCH conditioned that mobility and HO related requirements can be met
  Note: RAN1 assumes that RAN2 will check against to RAN2 requirements

## Slide 4: Background
TR38.804
  Each cell on which the UE is allowed to camp broadcasts at least some contents of the minimum SI, while there may be cells in the system on which the UE cannot camp and do not broadcast the minimum SI. For a cell/frequency that is considered for camping by the UE, the UE should not be required to acquire the contents of the minimum SI of that cell/frequency from another cell/frequency layer. This does not preclude the case that the UE applies stored SI from previously visited cell(s). If the UE cannot determine the full contents of the minimum SI of a cell (by receiving from that cell or from valid stored SI from previous cells), the UE shall consider that cell as barred. It is desirable for the UE to learn very quickly that this cell cannot be camped on.

## Slide 5: Proposal (1/3)
Following contents are carried in NR-MIB
  (Part of) SFN: [7 - 10] bits
    At least 80 ms granularity
      FFS: indication within 80 ms
  [H-SFN: 10 bits]
    RAN1 will ask RAN2
  Timing information within radio frame: [0 - 7] bits
    E.g., SS block time index: [0 - 6] bits
    E.g., half radio frame timing: [0 - 1] bit
  RMSI scheduling information: [x] bits
    CORESET(s) information: [x] bits
      Simplified information of CORESET(s) compared to CORESET(s) information for UE-specific configuration is considered
      E.g., Time/frequency resource configuration of CORESET(s)
      [Numerology of RMSI: [0 - 2] bits]
    [Information regarding frequency resources for PDSCH scheduling: [x] bits]
  [Information regarding bandwidth part: [x] bits]

## Slide 6: Proposal (2/3)
  [Information for quick identification that UE cannot camp on the cell (e.g., RMSI presence flag): [0 - 1] bit]
    RAN1 will ask RAN2
  [SS burst set periodicity: [0 - 3] bits]
  [Information on actual transmitted SS block(s): [0 - x] bits]
  [Area ID: x bits]
    RAN1 will ask RAN2
  [Value tag: x bits]
    RAN1 will ask RAN2
  [cell ID extension: x bits]
    RAN1 will ask RAN2
  [Information on tracking RS: x bits]
  Reserved bits: [x > 0] bits
CRC size for NR-MIB is [16 + y] bits

## Slide 7: Proposal (3/3)
RAN1 targets design of NR-PBCH payload size to be no larger than 72 bits and no less than 40 bits including CRC.
  Note: Based on the performance evaluation done so far, the upper limit range is between 72 and 48 bits