## Slide 1
3GPP TSG RAN WG1 Meeting #89 R1-1709797 Hangzhou, China, 15th - 19th May 2017
Agenda item: 7.1.2.4.1
WF on CSI-RS pattern for beam management
Huawei, HiSilicon, CATT, ZTE, OPPO

## Slide 2: Background
Following agreements have been made in RAN1#88bis:
Agreements:
At least for CSI-acquisition, for density 1 RE/port/PRB, X<8, and N=1 or 2 OFDM symbol, support X-port CSI-RS resource composed of M adjacent RE(s) in the frequency domain and N adjacent RE(s) in the time domain
  FFS X=1
  X=2: (M, N)= (2, 1) , FFS (1, 2)
  X=4: (M, N)= (4, 1) , (2, 2)
  FFS N > 2
  FFS: RE patterns for beam management
FFS: the RE pattern for an X-port CSI-RS resource when X>=8
FFS: the number of component CSI-RS RE patterns for X>=8-port CSI-RS resources
Strive to minimize the possible pairs of (Y,Z) for the component CSI-RS RE patterns while considering configuration complexity and overhead
Agreements:
At least CSI-RS for CSI acquisition, NR supports CSI-RS density d RE/RB/port for x-port CSI-RS
  Value(s) of d are at least d=1,1/2.
  For d<1, PRB-level comb-type transmission is supported.
    FFS whether offset value(s) can be the same or different across antenna ports
  FFS on supporting d>1 in the consideration of use case, e.g., NZP CSI-RS for IMR.
  FFS on the supported combinations of value(s) of x and d.
For an X-port CSI-RS resource, at least for X = 1, support density D >= 1 RE/port/PRB
  FFS: Support for D > 1 for other values of X
  Note: For X = 1, CDM code value(s) assumed to be 1

## Slide 3: Proposal
For beam management, reuse at least following X-port CSI-RS patterns of one OFDM symbol for CSI acquisition
  X=1 and 2
    FFS: other value(s) of X
  If larger subcarrier spacing is supported when sub-time units smaller than an OFDM symbol in reference numerology, reuse the above pattern(s) in one sub-time unit
  If IFDMA is supported when sub-time units smaller than an OFDM symbol in reference numerology, the non-zero power RE pattern in one OFDM symbol is comprised of 1-port CSI-RS patterns
FFS: density of CSI-RS for beam management