## Slide 1: WF on LTE-NR Coexistence with UL sharing
Huawei, HiSilicon, AsusTek, CATR, MediaTek, vivo, Spreadtrum, [Intel],[Apple],[Samsung],[OPPO]
3GPP TSG RAN WG1 #89 Meeting R1-1709807
Hangzhou, China, 15-19 May 2017
Agenda item: 7.1.8

## Slide 2: Background
In NR WID:
NR-LTE co-existence mechanisms [RAN1, RAN2, RAN4];
- Support co-existence of LTE UL and NR UL within the bandwidth of an LTE component carrier and co-existence of LTE DL and NR DL within the bandwidth of an LTE component carrier, and identify and specify at least one NR band/LTE-NR band combination for this operation.
- Minimize impact to NR physical layer design to enable this co-existence.
- No impact to the ability of legacy LTE devices to operate on the LTE carrier co-existing with NR
- No implication that UE has to support simultaneous connection of NR and LTE in the bandwidth of an LTE component carrier

## Slide 3: Background
RAN4 Agreements:
  The following Frequency ranges are to be defined for LTE-NR coexistence with UL sharing
  *: The exact frequency range around 3.5GHz may be revised during R15 NR WI
  Note: The LTE-NR dual connectivity UE RF requirements with the same frequency ranges can be reused as the starting point for the above NR paired band.
Frequency ranges for NR | Operators whose request is included in the frequency range
1710-1785MHz (UL)/3.3-4.2 GHz*(DL&UL) | China Telecom, China Unicom, CMCC, Deutsche Telekom
832-862MHz (UL)/3.3-4.2 GHz*(DL&UL) | Orange, Telefonica, Etisalat, Deutsche Telekom
880-915MHz (UL)/3.3-4.2 GHz*(DL&UL) | CMCC
703-748MHz (UL)/3.3-4.2 GHz* (DL&UL) | Orange, Telefonica, Etisalat

## Slide 4: Background
RAN1 Agreements:
For NR NSA for a UE, NR supports the case that when the UE is configured with multiple UL carriers on different frequencies (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency), the UE operates on only one of the carriers at a given time among a pair of LTE and NR carriers
  FFS whether or not there is specification impact
    If there is RAN1 specification impact, aim to minimize the specification impact for NR
    Note: this feature by itself is not intended to have any LTE RAN1 specification impact
  Note: the other case of allowing simultaneous operation on two or more UL carriers is already agreed to be supported

## Slide 5: Background
RAN1 Agreements:
Specify mechanisms for supporting supplementary Uplink frequency
  Note: SUL herein refers to the case when there is only UL resource for a carrier from NR perspective
  Use SUL as complimentary access link (including from random access point of view) to NR TDD and to NR FDD, where the UE may select PRACH resources either in the NR TDD/FDD uplink frequency or the SUL frequency.
  Note: The SUL frequency can be a frequency shared with LTE UL(at least for the case when NR spectrum is below 6 Ghz).
    Minimize impact to NR physical layer design to enable this co-existence
  Note: whether or not UE has to support simultaneous transmission on uplink frequencies is a separate discussion
Sent LS accommodating above agreement to RAN2 and RAN4

## Slide 6: Proposal
For NR standalone operation for a UE,
  NR supports the case that the UE is configured with UL carriers on different frequency ranges and the UE can only transmit on one of the carriers at a given time.
    One of the carrier frequencies can be a frequency shared with LTE UL (at least for the case when NR spectrum is below 6 GHz).