## Slide 1: WF on evaluation assumption on UL transmission without UL grant in a DCI
LG Electronics, NICT, …
R1-1709824
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda Item: 7.1.3.3.2

## Slide 2: Background
From TR 38.802, we can use following values or assumptions for evaluation for UL transmission without grant in a DCI
  Table 9.1.2-2: Link-level evaluation assumptions in TR 38.802 9.1.2 Performance evaluation of multiple access
Parameters | Values or assumptions | Further specified values reported
Carrier Frequency | 2 GHz | 
Waveform | OFDM /SC-FDMA Other waveform is not precluded | OFDMA with equal bandwidth and distributed subcarrier allocation or OFDMA with orthogonal Walsh code
Numerology | Same as Release 13 | 
System Bandwidth | 10 MHz | Allocated bandwidth reported: 4RB, 6RB, 12RB The same for non-orthogonal MA and OFDMA
Target spectral efficiency | Proponents report per UE spectral efficiency and the number of UEs multiplexed if multi-UEs LLS is assumed | The same target per UE spectral efficiency for non-orthogonal MA and OFDMA Without short-term (per TTI) MCS adaptation Detail of reported target SE per user and the number of users are listed in Table 3
BS antenna configuration | 2/4 Rx as baseline 8Rx optional | See Table 3
UE antenna configuration | 1Tx | 
Transmission mode | TM1 (refer to TS36.213) | 
SNR distribution of Multiple UEs | Proponents report if single-user or multi-user LLS is used, and what SNR distribution is assumed. | Either equal long-term SNR and/or unequal long-term SNR has been considered Detail of assumptions listed in Table 3
Propagation channel & UE velocity | TDL for in TR38.900 as mandatory EPA, EVA, ETU as optional 3km/h, 30km/h, 120km/h | See Table 3
Max number of HARQ transmission | 1, 4 | 1
Channel estimation |  | Either ideal and/or realistic channel estimation has been considered Detail of assumptions listed in Table 3
MA signature allocation |  | Either fixed and/or random MA signature (e.g., codebook, sequence, interleaver, etc.) allocation has been considered Detail of assumptions listed in Table 3
Timing/frequency offset |  | Frequency offset not considered Timing offset of either within CP and/or beyond CP has been considered Detail of assumptions listed in Table 3
SNR definition |  | SNR is either defined at the transmitter per layer or at the receiver as the sum per RE

## Slide 3: Background
From TR 38.802, we can use following values or assumptions for evaluation for UL transmission without grant in a DCI
  Table A.1.4-1: Simulation assumptions for URLLC in TR 38.802 A.1.4 Simulation assumption related to URLLC evaluation
Attributes | Values or assumptions
Carrier Frequency | 700MHz and 4 GHz (FDD and TDD)
Modulation and coding rate | QPSK, 16QAM, 64QAM 1/12, 1/6, 1/3 Other MCS not precluded Comparison should be made for the same spectrum efficiency
User bandwidth | Companies report
Latency bound | 1ms Other values are not precluded Companies report delay assumptions according to Table 1 in R1-166485
SINR range | -5dB to 20dB Larger range is not precluded
Sub-carrier spacing | Companies report
TTI length | Companies report
OFDM symbols per TTI | Companies report
Channel model | TDL/CDL in TR38.900; user speed = 3km/h, 15km/h (other user speed is not precluded)
BS antenna configuration | 2/4/8 Tx/Rx ports as start point Other values (i.e., up to 256) are not precluded
UE antenna elements | 2/4 Tx/Rx ports as start point Other values (i.e., up to 8) are not precluded
Packet arrive rate | Option 1: periodically Option 2: Poisson arrival with arrival rate l
PHY Packet size | 32 byte, 50 byte, 200 byte Other values are not precluded.
ACK Feedback assumption | Ideal as start point NOTE: It is also possible that no ACK feedback is needed,
Channel estimation | Ideal as start point; Realistic is not precluded when RS design is ready
CQI feedback assumption | Companies report the feedback scheme if any

## Slide 4: Background
From contributions in RAN1#89, R1-1707053, R1-1707655, There are still some parameters which can effect on performance of UL transmission without grant in a DCI

## Slide 5: Proposal
For evaluation on UE detection performance for UL transmission without grant in a DCI,
  assumptions given by the table below can be used additionally
    Other parameters are not precluded
  following KPIs can be used for measuring performance
    False alarm rate: The probability that the gNB detects a UE when the UE does not perform UL transmission without grant in a DCI
    Miss detection rate: The probability that the gNB does not detect a UE when the UE performs UL transmission without grant in a DCI
    Multiplexing capacity: How many the number of UE can share same resource
Parameters | Values
Subcarrier spacing | 15Khz as start point , other value can be provided by companies
Target SNR | 0 dB, 6 dB, other value can be provided by companies
Power control accuracy | ±0 dB, ±3 dB as start point, ±6 dB, ± 9 dB is optional
TA accuracy | ±0 CP, ±0.25 CP as start point, other value can be provided by companies
Channel estimation | Real estimation
UE detection mechanism | Provided by company