## Slide 1: Way forward on NPSS and NSSS in TDD NB-IoT
Huawei, HiSilicon, [….]
R1-1714725
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, August 21-25, 2017
Agenda item 5.2.7.6.1

## Slide 2: Background
In RAN#76, the WID on further NB-IoT enhancements was updated. One of the objectives is shown as follows:
  Support for TDD [RAN1, RAN2, RAN4]
    Specify TDD support for in-band, guard-band, and standalone operation modes of NB-IoT. The design shall assume no UL compensation gaps are needed by UE, and strive towards a common design among the deployment modes.
      Relaxations of MCL and/or latency and/or capacity targets to be considered by RAN1.
      Baseline is to support the same features as Rel-13 NB-IoT, additionally considering small-cells scenarios

## Slide 3: Proposals
  For NPSS/NSSS transmission in TDD NB-IoT:
    The period of NPSS and NSSS are the same with FDD NB-IoT.
    NPSS is transmitted in SF5 of every radio frame and NSSS is transmitted in SF0 of every even-numbered radio frame.
    The signal design of NPSS and NSSS is the same with FDD.
    Duplex mode is indicated by different time separation between NPSS and NSSS than is used in FDD.