## Slide 1: Way forward on special subframe in TDD NB-IoT
Huawei, HiSilicon, [….]
R1-1714727
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, August 21-25, 2017
Agenda item 5.2.7.6.3

## Slide 2: Background
In RAN#76, the WID on further NB-IoT enhancements was updated. One of the objectives is shown as follows:
  Support for TDD [RAN1, RAN2, RAN4]
    Specify TDD support for in-band, guard-band, and standalone operation modes of NB-IoT. The design shall assume no UL compensation gaps are needed by UE, and strive towards a common design among the deployment modes.
      Relaxations of MCL and/or latency and/or capacity targets to be considered by RAN1.
      Baseline is to support the same features as Rel-13 NB-IoT, additionally considering small-cells scenarios

## Slide 3: Proposals
  On special subframe configuration in TDD NB-IoT:
    Strive to support as many LTE special subframe configurations as possible
  DwPTS is used for at least NPDSCH transmission.
    FFS the resource mapping details, i.e. puncturing or rate matching
    FFS for other DL physical channels and signals
  FFS possible use(s) of UpPTS for NPRACH, NPUSCH