## Slide 1: WF on Bit-Level Interleaver
MediaTek, CATT, InterDigital, ITRI, Samsung, ZTE, …
R1-1714728
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017
Agenda item 6.1.4.1.4

## Slide 2: Background (1)
Agreement:
If bit-level interleaving is applied, it should be limited to each code block individually
Conclusion for bit-level interleaving: Revisit after the decision on modulation symbol interleaving in the MIMO session.

## Slide 3: Background (2)
In appendix, we showed the gain of bit-level interleaver is independent of channel delay spread
In this meeting, [1]-[8] proposed bit-level interleavers.
  Some showed the gain of bit-level interleaver
  More reliable modulation bits on LDPC systematic bits to explore constellation gain

## Slide 4: Proposal
Bit-level interleaver can be directly discussed in coding session, since frequency interleaver and bit-level interleaver can be decoupled.
Bit-level interleaver should be supported at least in high order modulation schemes.

## Slide 5: References
[1] R1-1712177, Interleaving for eMBB data, Huawei
[2] R1-1712431, Bit-level interleaving for NR LDPC, CATT
[3] R1-1713209, On bit-level interleaver, LG
[4] R1-1713230, On interleaving for LDPC code, ZTE
[5] R1-1713461, Bit-level interleaving, QC
[6] R1-1713660, Bit-level interleaver of LDPC codes on high order modulation, Samsung
[7] R1-1713710, On design of bit-level interleaver, MediaTek
[8] R1-1714374, Interleaving for LDPC, Nokia

## Slide 6: Appendix

## Slide 7: Performance Comparison of Bit-Level Interleaver with Different Delay Spread
Info size (bits) | Modulation | CR | 25ns | 200ns | 1600ns
6144 | 16QAM | 1/3 | Gain = 0.12 dB | 0.12 | 0.1
6144 | 16QAM | 2/3 | 0.08 | 0.09 | 0.09
6144 | 64QAM | 1/3 | 0.36 | 0.36 | 0.27
6144 | 64QAM | 2/3 | 0.16 | 0.21 | 0.13
6144 | 256QAM | 1/3 | 1.1 | 1.05 | 0.94
6144 | 256QAM | 2/3 | 0.45 | 0.43 | 0.49
TDL-B Channel
Gain of bit-level interleaver is independent of delay spread or channel.