## Slide 1: WF on QCL and PDSCH RE Mapping for NC-JT
ZTE..
R1-1714730
3GPP TSG RAN WG1 Meeting #90
Prague, Czechia 21st – 25th August 2017
Agenda item 5.2.4.1

## Slide 2: Background
In RAN1#89, the following agreements have been achieved on QCL and PDSCH RE Mapping:
  FFS additional support of non overlapping RA from different CWs taking into account the following issues:
    Performance of non overlapping RA comparing to the existing CoMP schemes
    DCI payload
  The existing PDSCH-RE-MappingQCL is extended by allowing configuration of the 2nd set of following parameters
    CRS port number
    CRS shift
    MBSFN configuration
    ID of ZP CSI-RS ID
    ID NZP CSI-RS for QCL
  UE should assume the same PDSCH start for the 1st and 2nd sets

## Slide 3: Proposal
Non-overlapping resource allocation is supported
  RRC signalling is supported to configure independent indication of RA corresponding to 2 CWs is supported within one RA field. When it is configured,
    The scheduling granularity is twice coarser. i.e. The new RBG size is twice of the original RBG size.
    QCL and PDSCH RE mapping in allocated resources corresponding to CW k is done only according to the PQI parameter set of CW k, where k=1,2
  Align MBSFN configuration for two CWs
    UE should assume the same MBSFN configuration for 1st and 2nd sets of PQI parameters