## Slide 1: WF on system level evaluations 1024QAM
Intel, …
R1-1714741
3GPP TSG RAN WG1 Meeting #90
Prague, P.R. Czech 21th – 25th August 2017
Agenda item 5.2.5.1

## Slide 2: General observations
Three out of four sources (e.g. R1-1712091 - Huawei, R1-1712495 - Intel, R1-1708793 - QC) shows the performance loss due to 1024QAM for some SNRs in the link-level evaluations
In LS R1-1708793, RAN4 indicates that lower Tx EVM can be achieved by using additional power backoff at the transmitter (“Support of such TX EVM values could result in some power back-off and/or relaxed clipping at the cost of decreased coverage, increased price and size.”) that was not accounted in the current studies of 1024QAM
In the previous studies on the higher order modulation the performance benefits of higher order modulation depends on the CRS interference presence and achievable SINR on the system level

## Slide 3: Proposal
1024QAM feasibility study shall include system level evaluation that takes into account practical impairments (Tx/Rx EVMs, additional power backoff, etc) and realistic interference modelling from other TPs (e.g. CRS interference)
The proposed SLS assumptions for 1024QAM evaluations are provided (see next slide)

## Slide 4
Parameters | Value |  | 
Type | Indoor hotspot |  | 
Layout | Indoor TPs: 2BSs per 120m x 50m |  | 
Tx/Rx EVM | According to R1-1708793 |  | 
Minimum distances | Same as in TR 36.872 |  | 
Carrier frequency | 3.5GHz |  | 
System bandwidth | 10MHz (50RBs) |  | 
Channel model | Indoor Hotspot (see TR 36.872) |  | 
BS Tx power | 24dBm (Power backoff is applied for 1024QAM) |  | 
BS antenna pattern | 2D omni with 5dBi gain (TR 36.872) |  | 
BS antenna height | 3m |  | 
UE antenna height | 1.5m |  | 
UE antenna gain | See TR 36.872 |  | 
UE receiver noise figure | 9 dB |  | 
Traffic model | Non full buffer FTP traffic model 1, S = 0.5Mbytes |  | 
Traffic load (target RU) | <5%, 20%, 40%, 60% |  | 
UE receiver | MMSE-IRC as the baseline receiver |  | 
UE antennas | 2Tx, 4Tx |  | 
Feedback assumption | PUSCH 3-1 |  | 
Number of CSI-RS ports | 2, 4 |  | 
Interference modeling | Yes (including interference from CRS) |  | 
Channel estimation | Realistic |  |