## Slide 1: WF on UE-UE CLI measurement
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #90 R1-1714743
Prague, Czech Republic, 21-25 August 2017
Agenda item: 6.1.5.1

## Slide 2: Background
Agreements:
For CLI management, support UE-to-UE interference measurement and reporting without the introduction of new RS(s)
Agreements:
For UE-to-UE interference, support CLI measurement metrics which include at least one of
  RSRP for the purpose of CLI
    FFS the definition (e.g., based on SRS, DM-RS, etc.) and the corresponding reporting
  RSSI for the purpose of CLI
    FFS the definition (e.g., resources for the measurement) and the corresponding reporting
For UE-to-UE interference, FFS additionally support CQI/CSI as the CLI measurement metrics and if so, its definition/reporting
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Proposal
Details of long term CLI-RSRP for UE-UE CLI measurement
  Definition of CLI-RSRP:
    Linear average over the power contributions of the resource elements that carry SRS configured for CLI measurements within the considered measurement frequency bandwidth in the time resources in the configured CLI measurement occasions
  At least NR SRS is used for UE-UE CLI measurement
    UE can be configured to transmit SRS for UE-UE CLI measurement
    UE can be configured with SRS resource(s) (including time-frequency resource(s), sequence(s), cyclic shift(s), periodicity, etc) to measure UE-UE CLI interference.
    Transmission timing advance of SRS for CLI measurement can be different from the transmission timing advance of its PUSCH, e.g. D2D channel transmission timing
    Mechanism to avoid potential DL transmission interfering the SRS for UE-UE CLI measurement is supported
      FFS exact details, e.g. by rate matching the DL transmission around the SRS
    Mechanism to limit the UE complexity for UE-UE CLI measurement is supported
      FFS exact details, e.g. by limiting the number of root sequence of SRS for UE-UE CLI measurement that a UE needs to detect within a certain amount of time, longer periodicity.
    FFS: L3 filtering for the CLI RSRP
  Higher layer reporting is used to report UE-UE CLI measurement result
    Mechanism to reduce reporting overhead is supported
      FFS e.g. conditional reporting by a threshold, reporting the maximum few CSI measurement

## Slide 4: Proposal
Details of long term CLI-RSSI for UE-UE CLI measurement
  Definition of CLI-RSSI:
    The linear average of the total received power observed only in certain OFDM symbols of measurement time resources, in the measurement bandwidth, over the configured resource elements for CLI measurement by the UE from all sources.
  At least NR SRS is used for UE-UE CLI measurement
    UE can be configured to transmit SRS for UE-UE CLI measurement
    UE can be configured with SRS time-frequency resource(s) to measure UE-UE CLI interference
    Transmission timing advance of SRS for CLI measurement can be different from the transmission timing advance of its PUSCH, e.g D2D channel transmission timing
    Mechanism to avoid potential DL transmission interfering the SRS for UE-UE CLI measurement is supported
      FFS exact details, e.g. by rate matching the DL transmission around the SRS
  Higher layer reporting is used to report UE-UE CLI measurement result
    Mechanism to reduce reporting overhead is supported
      FFS e.g. conditional reporting by a threshold, reporting the maximum few RSSI CLI measurement

## Slide 5: Proposal
Details of short term CLI-RSSI for UE-UE CLI measurement
  Definition of CLI-RSSI:
    The total received power observed only in certain OFDM symbols of measurement time resources, in the measurement bandwidth, over the configured resource elements for CLI measurement by the UE from all sources.
  Detailed configuration
    Measurement time-frequency resource
    Trigger scheme.
  Physical layer reporting is used to report UE-UE CLI measurement result
    Mechanism to reduce reporting overhead is supported
      FFS e.g. conditional reporting by a threshold, reporting the maximum few RSSI CLI measurement
      FFS e.g. for the continuous CSI measurement report per measurement, reporting the CSI measurement result with varying larger than another threshold