## Slide 1: Way forward on further details of Cat. 3 solution for NPRACH cell range enhancement
Huawei, HiSilicon,[….]
R1-1714751
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, August 21~25, 2017
Agenda item 5.2.7.3

## Slide 2: Background
In RAN1#89, it was agreed that:
To support of cell range of at least 100 km, FFS between:
    Cat 1: Rel-13 NPRACH
    Cat 2: Sharing the same NPRACH resources as Rel-13 NPRACH formats, with symbol or symbol-group level scrambling; maintaining feasibility of FFT processing and orthogonality of preambles on different tones
    CP length FFS between same as or longer than Rel-13 formats
    Cat 3: New NPRACH numerology with CP length FFS between same as or longer than Rel-13 formats
      Option A: 1.25 kHz subcarrier spacing with minimum hop distance of 1.25 kHz
      Option B: 3.75 kHz subcarrier spacing with minimum hop distance 1.25 kHz
      Option C: 3.75 kHz subcarrier spacing with minimum hop distance 3.75 kHz with new hopping pattern
    Combinations of Category 2 and Category 3 solutions are not precluded.

## Slide 3: Proposals
For further consideration of Category 3 solutions for NPRACH cell range enhancement, the new numerology in Category 3 is based on:
  1.25 kHz subcarrier spacing with minimum hop distance of 1.25 kHz
  CP length is 800us
  Other details are FFS.