## Slide 1: Ncs for Preamble Generation for PRACH Preamble Format 0-3
LG Electronics, ZTE, InterDigital, NTT DOCOMO
R1-1714801
3GPP TSG RAN WG1 Meeting RAN1 #90
Prague, Czech Republic 21st – 25th August 2017
Agenda item: 6.1.1.4.1

## Slide 2: Background
Agreement : (RAN1#90)
For NR PRACH preamble L=839 with SCS = 1.25 kHz, Ncs restricted set type B is supported in addition to restricted set type A
For NR PRACH preamble L=839 with SCS 5kHz, Ncs restricted set type A and type B are supported

## Slide 3: Background
Ncs for Preamble generation for PRACH preamble format 0-3 captured in TS38.211
Editor’s Memo: “Is the intention to have the same values as in LTE?”

## Slide 4: Observation
For preamble format 0-2
  All of indices are available for PRACH preamble format 0-2.
Zerocorrelation Zone Config | PRACH preamble with length of 839 / 1.25kHz SCS |  |  |  |  | 
 | Unrestricted Set | Max.cell (km) | Restricted Set A | Max.cell (km) | Restricted Set B | Max.cell (km)
0 | 0 |  | 15 | 1.08 | 15 | 1.08
1 | 13 | 0.79 | 18 | 1.51 | 18 | 1.51
2 | 15 | 1.08 | 22 | 2.08 | 22 | 2.08
3 | 18 | 1.51 | 26 | 2.65 | 26 | 2.65
4 | 22 | 2.08 | 32 | 3.51 | 32 | 3.51
5 | 26 | 2.65 | 38 | 4.37 | 38 | 4.37
6 | 32 | 3.51 | 46 | 5.51 | 46 | 5.51
7 | 38 | 4.37 | 55 | 6.8 | 55 | 6.8
8 | 46 | 5.51 | 68 | 8.66 | 68 | 8.66
9 | 59 | 7.37 | 82 | 10.66 | 82 | 10.66
10 | 76 | 9.8 | 100 | 13.24 | 100 | 13.24
11 | 93 | 12.24 | 128 | 17.24 | 118 | 15.81
12 | 119 | 15.95 | 158 | 21.53 | 137 | 18.53
13 | 167 | 22.82 | 202 | 27.83 |  | 
14 | 279 | 38.84 | 237 | 32.83 |  | 
15 | 419 | 58.86 |  |  |  | 
Max Cell coverage = ROUND(((((Ncs -ng)*Teq/Nzc)-Delay)*3/10/2),2) , where, ng=2, Teq=800, Nsc=839, Delay=5.2

## Slide 5: Observation
For preamble format 3
  Lower part of indices are available for PRACH preamble format 3.
Zerocorrelation Zone Config | PRACH preamble with length of 839 / 5kHz SCS |  |  |  |  | 
 | Unrestricted Set | Max.cell (km) | Restricted Set A | Max.cell (km) | Restricted Set B | Max.cell (km)
0 | 0 |  | 15 |  | 15 | 
1 | 13 |  | 18 |  | 18 | 
2 | 15 |  | 22 |  | 22 | 
3 | 18 |  | 26 | 0.08 | 26 | 0.08
4 | 22 |  | 32 | 0.29 | 32 | 0.29
5 | 26 | 0.08 | 38 | 0.51 | 38 | 0.51
6 | 32 | 0.29 | 46 | 0.79 | 46 | 0.79
7 | 38 | 0.51 | 55 | 1.12 | 55 | 1.12
8 | 46 | 0.79 | 68 | 1.58 | 68 | 1.58
9 | 59 | 1.26 | 82 | 2.08 | 82 | 2.08
10 | 76 | 1.87 | 100 | 2.72 | 100 | 2.72
11 | 93 | 2.47 | 128 | 3.73 | 118 | 3.37
12 | 119 | 3.4 | 158 | 4.8 | 137 | 4.05
13 | 167 | 5.12 | 202 | 6.37 |  | 
14 | 279 | 9.12 | 237 | 7.62 |  | 
15 | 419 | 14.13 |  |  |  | 
Max Cell coverage = ROUND(((((Ncs -ng)*Teq/Nzc)-Delay)*3/10/2),2) , where, ng=2, Teq=800, Nsc=839, Delay=5.2

## Slide 6: Proposal
Same cyclic shift values as defined in LTE is applied for NR PRACH preamble format 0-3.
  NOTE: For NR PRACH preamble format 3, lower part of indices (e.g from 6 to 15) in the Table 6.3.3.1-3 are used for configuration of cyclic shift.

## Slide 7: Appendix