## Slide 1: WF on Remaining Details of Channel Modeling
Ericsson, Nokia, Nokia Shanghai Bell
R1-1714822
3GPP TSG RAN WG1 Meeting #90
Prague, CZ, 21st – 25th August 2017
Agenda item 5.2.8.3

## Slide 2: Background
In RAN1#89 and the follow up email discussions, agreements were reached on wide aspects of channel modelling for RMA-AV, UMa-AV and UMi-AV
However, there are still some remaining working assumptions need to be confirmed: a missing RMA-AV NLOS shadowing for aerial UEs below 10m, and a proposed correction on UMA-AV NLOS pathloss for UEs above 22.5m during the offline calibration
Also, during the offline calibration, some questions were raised on what O2I penetration loss should be used

## Slide 3: Proposals
Proposal 1: Confirm the following working assumptions that were made in RAN1#89 and/or the follow-up email discussion.
  LOS pathloss for UMi-AV for aerial UE heights above 22.5m
  NLOS pathloss for UMi-AV for aerial UE heights above 22.5m
  LOS shadowing for UMa-AV for aerial UE above 22.5m
  LOS shadowing model for RMa-AV for aerial UE s above 10m
  NLOS shadowing for RMa-AV for aerial UE above 10m
Proposal 2: Adopt the following correction for NLOS pathloss for UMa-AV for aerial UE heights above 22.5m
Proposal 3:
  Reuse TR38.901 for RMa-AV NLOS shadowing for aerial UE heights below 10m
Proposal 4:
  For outdoor terrestrial UEs of 30km/h, car penetration loss is according to Section 7.4.3.2 in TR38.901
  For UMa-AV/UMi-AV indoor terrestrial UEs, use the building penetration model in Table 7.4.3-3 of TR38.901 for O2I penetration loss.
  For RMa-AV indoor terrestrial UEs, use the low-loss model in Table 7.4.3-2 of TR38.901 for O2I penetration loss
  For aerial UE, no penetration loss is added