## Slide 1: WF on Power Control for FeD2D
Intel, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #90 R1-1714849
Prague, Czech Republic, 21st – 25th August 2017
Agenda item - 5.2.9.2.3.3

## Slide 2: Background
Agreements from RAN1#89
  For sidelink power control for FeD2D, unless instructed by TPC command from the eNB, the UE transmits at a power no larger than the calculated power based on open loop power control between the UE and the eNB as described in Section 14.1.1.5 of TS 36.213
    Maximum power of sidelink transmission, and open loop power control parameters (P0, alpha) are configured by eNB.
    For out of coverage operation power control parameters (P0, alpha = 0) can be pre-configured
    FFS if UE is not required to monitor DL
  UE can set transmit power below the upper limit based on UE-UE channel propagation conditions
    FFS details and specification impact (e.g. whether the power setting can be up to UE implementation or mandated by specification)

## Slide 3: Proposal
Relay and Remote UEs exchange information to control transmit power adjustments of each other using power control commands
  Note: Details of measurements and information exchanged over sidelink are determined in the work item phase (e.g. sidelink PHR)